## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Components of a Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 3
Processor-DRAM Gap (Latency)
1980 microprocessor executes ~one instruction in same time as DRAM access
2017 microprocessor executes ~1000 instructions in same time as DRAM access
Slow DRAM access has disastrous impact on CPU performance!

## Slide 4
Typical Memory Hierarchy
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Second-Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s-1000 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)

## Slide 5
Big Idea: Locality
Temporal Locality (locality in time)
  Go back to same book on desk multiple times
  If a memory location is referenced, then it will tend to be referenced again soon
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books on J.D. Salinger since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon

## Slide 6
Adding Cache to Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 7
Pipelined RISC-V RV32I Datapath (with I,D$)
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
Must pipeline instruction along with data, so control operates correctly in each stage

## Slide 8
CPU-Cache Interaction (5-stage pipeline)
PC
addr
inst
Primary
Instruction
Cache
0x4
Add
IR
D
bubble
hit?
Decode,
Register
Fetch
wdata
R
addr
wdata
rdata
Primary
Data
Cache
we
A
B
Y
Y
ALU
MD1
MD2
Cache Refill Data from Lower Levels of Memory Hierarchy
hit?
Stall entire CPU on data cache miss
To Memory Control
M
E

## Slide 9
Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Address
Tag
Data Block
Data
Byte
Data
Byte
Data
Byte
Line
100
304
6848
copy of main
memory
location 100
copy of main
memory
location 101
416

## Slide 10
Cache Terminology
hit: data appears in some block
  hit rate: the fraction of accesses found in the level
  hit time: time to access the level (consists of RAM access time + time to determine hit)
miss: data needs to be retrieved from a block in the lower level (e.g., block Y)
  miss rate = 1 - (hit rate)
  miss penalty: time to replace a block in the upper level + time to deliver the block to the processor
hit time << miss penalty
Abbreviation: “$” = cache (a Berkeley innovation!)

## Slide 11
Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
AMAT = Time for a hit + Miss rate × Miss penalty
miss penalty: time to fetch a block from lower memory level
  access time: function of latency
  transfer time: function of bandwidth b/w levels
    transfer one “cache line/block” at a time
    transfer at the size of the memory-bus width
Important Equation!

## Slide 12
Peer Instruction
AMAT = Time for a hit + Miss rate × Miss penalty
Given a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache hit time of 1 clock cycle, what is AMAT?
A : ≤200 psec
B : 400 psec
C : 600 psec
D : ≥ 800 psec

## Slide 13
Processor Address Fields Used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2(number of sets)
Size of Tag = Address size – Size of Index – log2(number of bytes/block)
Block offset
Set Index
Tag
Processor Address (32-bits total)

## Slide 14
What Limits Number of Sets?
For a given total number of blocks, we save comparators if have more than two sets
Limit: As Many Sets as Cache Blocks => only one block per set – only needs one comparator!
Called “Direct-Mapped” Design
Block offset
Index
Tag

## Slide 15
Direct-Mapped Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 16
Direct Mapped Cache Example: Mapping a 6-bit Memory Address
In example, block size is 4 bytes/1 word
Memory and cache blocks always the same size, unit of transfer between memory and cache
# Memory blocks >> # Cache blocks
  16 Memory blocks = 16 words = 64 bytes => 6 bits to address all bytes
  4 Cache blocks, 4 bytes (1 word) per block
  4 Memory blocks map to each cache block
Memory block to cache block, aka index: middle two bits
Which memory block is in a given cache block, aka tag: top two bits
0
5
1
Byte Within Block
Byte Offset
2
3
Block Within $
4
Mem Block Within $ Block
Tag
Index

## Slide 17
One More Detail: Valid Bit
When start a new program, cache does not have valid information for this program
Need an indicator whether this tag entry is valid for this program
Add a “valid bit” to the cache tag entry
  0 => cache miss, even if by chance, address = tag
  1 => cache hit, if processor address = tag

## Slide 18
Cache Organization: Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the memory block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits (xx) define the byte in the block (32b words)
Index

## Slide 19
Direct-Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator

## Slide 20
Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 1K words
20
Tag
Index
8
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11. . . 4 . . . 0
Byte offset
20
Hit
What kind of locality are we taking advantage of?
2
Data
32
Word offset

## Slide 21
Ping Pong Cache Example: Direct-Mapped Cache w/4 Single-Word Blocks, Worst-Case Reference String
Consider the main memory address reference string of word numbers:
0 4 0 4 0 4 0 4
0
4
0
4
0
4
0
4
Start with an empty cache - all blocks initially marked as not valid

## Slide 22
Ping Pong Cache Example: Direct-Mapped Cache w/4 Single-Word Blocks, Worst-Case Reference String
Consider the main memory address reference string of word numbers:
0 4 0 4 0 4 0 4
0
4
0
4
0
4
0
4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping-pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses

## Slide 23
Example: 2-Way Set Associative $ (4 words = 2 sets x 2 ways per set)
0
Cache
Main Memory
Q: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)

## Slide 24
2-Way Set-Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t

## Slide 25
Ping Pong Cache Example: 4 Word 2-Way SA $, Same Reference String
Consider the main memory word reference string
0 4 0 4 0 4 0 4
0
4
0
4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping-pong effect in a direct-mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses

## Slide 26
Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
...
253
254
255
Data
Tag
V
0
1
2
...
253
254
255
Data
Tag
V
0
1
2
...
253
254
255
Index
Data
Tag
V
0
1
2
...
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3

## Slide 27
Alternative Cache Organizations
“Fully Associative”: Block can go anywhere
  First design in lecture
  Note: No Index field, but one comparator/block
“Direct Mapped”: Block goes one place
  Note: Only 1 comparator
  Number of sets = number blocks
“N-way Set Associative”: N places for a block
  Number of sets = number of blocks / N
  N comparators
  Fully Associative: N = number of blocks
  Direct Mapped: N = 1

## Slide 28
Types of Caches
type of cache | mapping of data from memory to cache | complexity of searching the cache
Direct mapped (DM) | a memory value can be placed at a single corresponding location in the cache | fast indexing mechanism
set- associative (SA) | a memory value can be placed in any of a set of locations in the cache | slightly more involved search mechanism
fully- associative (FA) | a memory value can be placed in any location in the cache | extensive hardware resources required to search (CAM)

## Slide 29
Describing Caches: 7 Parameters
access time: Thit
capacity
  total amount of data the cache can hold
    # of blocks × block size
block (line) size
  the amount of data that gets moved into or out of the cache as a chunk
    analogous to page size in virtual memory
replacement policy
  what data is replaced on a miss?
associativity
  how many locations in the cache is a given address eligible to be placed in?
unified, instruction, data
  what type of data is kept in the cache? We’ll cover this in more detail later

## Slide 30
Range of Set-Associative Caches
For a fixed-size cache and fixed block size, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number of ways) and halves the number of sets
  decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
Decreasing associativity, lower way, more sets
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity, higher way, less sets
Selects the set
Used for tag compare
Selects the word in the block
More Associativity (more ways)

## Slide 31
Example: Alternatives in an 8 Block Cache
Direct Mapped: 8 blocks, 1 way, 1 tag comparator, 8 sets
Fully Associative: 8 blocks, 8 ways, 8 tag comparators, 1 set
2 Way Set Associative: 8 blocks, 2 ways, 2 tag comparators, 4 sets
4 Way Set Associative: 8 blocks, 4 ways, 4 tag comparators, 2 sets
0
1
2
3
DM:
8 sets
1 way
4
5
6
7
0
1
2
3
FA:
1 set
8 ways
4
5
6
7
0
1
2
3
2 Way SA: 4 sets
Set 0
Set 1
Set 2
Set 3
4
5
6
7
0
1
2
3
4 Way SA: 2 sets
Set 0
Set 1
4
5
6
7

## Slide 32
Peer Instruction
For a cache with constant total capacity, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets could be doubled
B : The tag width could decrease
C : The block size could stay the same
D : The block size could be halved

## Slide 33
Example of Caches
given a 2MB, direct-mapped physical caches, line size=64bytes, and 52-bit physical address
  tag size?
  now change it to 16-way, tag size?
  how about if it’s fully associative, tag size?

## Slide 34
Total Cache Capacity =
Associativity * # of sets * block_size
Bytes = blocks/set * sets * Bytes/block
Byte Offset
Tag
Index
C = N * S * B
address_size = tag_size + index_size + offset_size
= tag_size + log2(S) + log2(B)
Double the Associativity: Number of sets?
tag_size? index_size? # comparators?
Double the Sets: Associativity?
tag_size? index_size? # comparators?

## Slide 35
Block Size and Spatial Locality
Block is unit of transfer between the cache and memory
Word3
Word0
Word1
Word2
Larger block size has distinct hardware advantages
  less tag overhead
  exploit fast burst transfers from DRAM
  exploit fast burst transfers over wide busses
What are the disadvantages of increasing block size?
block address offsetb
2b = block size a.k.a line size (in bytes)
Split CPU address
b bits
32-b bits
Tag
4 word block, b=2
Fewer blocks => more conflicts. Can waste bandwidth.

## Slide 36
Fully Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t

## Slide 37
Your Turn
For a cache of 64 blocks, each block four bytes in size:
The capacity of the cache is: ____ bytes.
Given a 2-way Set Associative organization, there are ___ sets, each of __ blocks, and __ places a block from memory could be placed.
Given a 4-way Set Associative organization, there are ____ sets each of __ blocks and __ places a block from memory could be placed.
Given an 8-way Set Associative organization, there are ____ sets each of __ blocks and ___ places a block from memory could be placed.

## Slide 38
Peer Instruction
For a cache with constant total capacity, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets is halved
B : The tag width decreases
C : The block size stays the same
D : The set index decreases

## Slide 39
Peer Instruction
For S sets, N ways, B blocks, which statements hold?
  The cache has B tags
  The cache needs N comparators
  B = N x S
  Size of Index = Log2(S)
A : (i) only
B : (i) and (ii) only
C : (i), (ii), (iii) only
D : All four statements are true

## Slide 40
Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). DM $: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
When miss occurs, which way’s block selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
    Must track when each way’s block was used relative to other blocks in the set
    For 2-way SA $, one bit per set → set to 1 when a block is referenced; reset the other way’s bit (i.e., “last used”)

## Slide 41
Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer

## Slide 42
Replacement Policy
In an associative cache, which block from a set should be evicted when the set becomes full?
Random
Least-Recently Used (LRU)
  LRU cache state must be updated on every access
  true implementation only feasible for small sets (2-way)
  pseudo-LRU binary tree often used for 4-8 way
First-In, First-Out (FIFO) a.k.a. Round-Robin
  used in highly associative caches
Not-Most-Recently Used (NMRU)
  FIFO with exception for most-recently used block or blocks
This is a second-order effect. Why?
Replacement only happens on misses

## Slide 43
Placement Policy
0 1 2 3 4 5 6 7
0 1 2 3
Set Number
Cache
Fully (2-way) Set Direct
Associative Associative Mapped
anywhere anywhere in only into
set 0 block 4
(12 mod 4) (12 mod 8)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
block 12
can be placed

## Slide 44
Benefits of Set-Associative Caches
Choice of DM $ versus SA $ depends on the cost of a miss versus the cost of implementation
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)

## Slide 45
Miss Rate vs. Cache Size on the Integer Portion of SPECCPU2000