## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Agenda
Parallel processing
Single instruction, multiple data
SIMD matrix multiplication
Amdahl’s law
Loop unrolling
Memory access strategy - blocking
And in Conclusion, …

## Slide 3
Reference Problem
Matrix multiplication
  Basic operation in many engineering, data, and imaging processing tasks
  Image filtering, noise reduction, …
  Many closely related operations
dgemm
  double-precision floating-point matrix multiplication

## Slide 4
Application Example: Deep Learning
Image classification (cats …)
Pick “best” vacation photos
Machine translation
Clean up accent
Fingerprint verification
Automatic game playing

## Slide 5
Matrices
Square matrix of dimension NxN
N-1
N-1
0
0

## Slide 6
Matrix Multiplication
C = A*B
Cij = Σk (Aik * Bkj)
A
B
C

## Slide 7
Reference: Python
Matrix multiplication in Python
N | Python [Mflops]
32 | 5.4
160 | 5.5
480 | 5.4
960 | 5.3
1 MFLOP = 1 Million floating-point operations per second (fadd, fmul)
dgemm(N …) takes 2*N3 flops

## Slide 8
C
c = a * b
a, b, c are N x N matrices

## Slide 9
Timing Program Execution

## Slide 10
C versus Python
N | C [GFLOPS] | Python [GFLOPS]
32 | 1.30 | 0.0054
160 | 1.30 | 0.0055
480 | 1.32 | 0.0054
960 | 0.91 | 0.0053
Which class gives you this kind of power?
We could stop here … but why? Let’s do better!
240x!

## Slide 11
Why Parallel Processing?
CPU Clock Rates are no longer increasing
  Technical & economic challenges
    Advanced cooling technology too expensive or impractical for most applications
    Energy costs are prohibitive
Parallel processing is only path to higher speed
  Compare airlines:
    Maximum speed limited by speed of sound and economics
    Use more and larger airplanes to increase throughput
    And smaller seats …

## Slide 12
Using Parallelism for Performance
Two basic ways:
  Multiprogramming
    run multiple independent programs in parallel
    “Easy”
  Parallel computing
    run one program faster
    “Hard”
We’ll focus on parallel computing in the next few lectures

## Slide 13
New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 14
Types of Parallelism
Parallelism in Hardware (Uniprocessor)
  Parallelism in a Uniprocessor
    Pipelining
    Superscalar, VLIW etc.
  SIMD instructions, Vector processors, GPUs
  Multiprocessor
    Symmetric shared-memory multiprocessors
    Distributed-memory multiprocessors
    Chip-multiprocessors a.k.a. Multi-cores
  Multicomputers a.k.a. clusters
Parallelism in Software
  Instruction level parallelism
  Task-level parallelism
  Data parallelism
  Transaction level parallelism

## Slide 15
Single-Instruction/Single-Data Stream (SISD)
Sequential computer that exploits no parallelism in either the instruction or data streams. Examples of SISD architecture are traditional uniprocessor machines
  E.g. our trusted RISC-V pipeline
Processing Unit
This is what we did up to now in this course

## Slide 16
Single-Instruction/Multiple-Data Stream (SIMD or “sim-dee”)
SIMD computer exploits multiple data streams against a single instruction stream to operations that may be naturally parallelized
  e.g., Intel SIMD instruction extensions or NVIDIA Graphics Processing Unit (GPU)
Today’s topic.

## Slide 17
Multiple-Instruction/Multiple-Data Streams (MIMD or “mim-dee”)
Multiple autonomous processors simultaneously executing different instructions on different data.
  MIMD architectures include multicore and Warehouse-Scale Computers
Instruction Pool
PU
PU
PU
PU
Data Pool
Succeeding topic and beyond.

## Slide 18
Multiple-Instruction/Single-Data Stream (MISD)
Different instructions on the same data
Fault-tolerant computers, Near memory computing (Micron Automata processor).
This has few applications. Not covered in this course

## Slide 19
Flynn* Taxonomy, 1966
SIMD and MIMD are currently the most common parallelism in architectures – usually both in same system!
Most common parallel processing programming style: Single Program Multiple Data (“SPMD”)
  Single program that runs on all processors of a MIMD
  Cross-processor execution coordination using synchronization primitives

## Slide 20
SIMD Applications & Implementations
Applications
  Scientific computing
    Matlab, NumPy
  Graphics and video processing
    Photoshop, …
  Big Data
    Deep learning
  Gaming
  …
Implementations
  x86
  ARM
  RISC-V vector extensions

## Slide 21
First SIMD Extensions: MIT Lincoln Labs TX-2, 1957

## Slide 22
x86 SIMD Evolution
New instructions
New, wider, more registers
More parallelism
http://svmoore.pbworks.com/w/file/fetch/70583970/VectorOps.pdf

## Slide 23
Laptop CPU Specs
$ sysctl -a | grep cpu
hw.physicalcpu: 2
hw.logicalcpu: 4
machdep.cpu.brand_string: Intel(R) Core(TM) i7-5557U CPU @ 3.10GHz
machdep.cpu.features: FPU VME DE PSE TSC MSR PAE MCE CX8 APIC SEP MTRR PGE MCA CMOV PAT PSE36 CLFSH DS ACPI MMX FXSR SSE SSE2 SS HTT TM PBE SSE3 PCLMULQDQ DTES64 MON DSCPL VMX EST TM2 SSSE3 FMA CX16 TPR PDCM SSE4.1 SSE4.2 x2APIC MOVBE POPCNT AES PCID XSAVE OSXSAVE SEGLIM64 TSCTMR AVX1.0 RDRAND F16C
machdep.cpu.leaf7_features: SMEP ERMS RDWRFSGS TSC_THREAD_OFFSET BMI1 AVX2 BMI2 INVPCID SMAP RDSEED ADX IPT FPU_CSDS

## Slide 24
SIMD Registers

## Slide 25
SIMD Data Types
(Now also AVX-512 available)

## Slide 26
SIMD Vector Mode

## Slide 27
Problem
Today’s compilers (largely) do not generate SIMD code
Back to assembly …
x86 (not using RISC-V as no vector hardware yet)
  Over 1000 instructions to learn …
  Green Book
Can we use the compiler to generate all non-SIMD instructions?

## Slide 28
x86 Intrinsics AVX Data Types
Intrinsics: Direct access to registers & assembly from C
Register

## Slide 29
Intrinsics AVX Code Nomenclature

## Slide 30
x86 SIMD “Intrinsics”
https://software.intel.com/sites/landingpage/IntrinsicsGuide/
4 parallel multiplies
2 instructions per clock cycle (CPI = 0.5)
assembly instruction

## Slide 31
Raw Double-Precision Throughput
Characteristic | Value
CPU | i7-5557U
Clock rate (sustained) | 3.1 GHz
Instructions per clock (mul_pd) | 2
Parallel multiplies per instruction | 4
Peak double FLOPS | 24.8 GFLOPS
Actual performance is lower because of overhead
https://www.karlrupp.net/2013/06/cpu-gpu-and-mic-hardware-characteristics-over-time/

## Slide 32
Vectorized Matrix Multiplication
Inner Loop:
for i …; i+=4
for j ...
i += 4

## Slide 33
“Vectorized” dgemm

## Slide 34
Performance
4x faster
But still << theoretical 25 GFLOPS!
N | Gflops | 
 | scalar | avx
32 | 1.30 | 4.56
160 | 1.30 | 5.47
480 | 1.32 | 5.27
960 | 0.91 | 3.64

## Slide 35
A trip to LA
Get to SFO & check-in | SFO  LAX | Get to destination
3 hours | 1 hour | 3 hours
Commercial airline:
Supersonic aircraft:
Get to SFO & check-in | SFO  LAX | Get to destination
3 hours | 6 min | 3 hours
Total time: 7 hours
Total time: 6.1 hours
Speedup:
Flying time Sflight = 60 / 6 = 10x
Trip time Strip = 7 / 6.1 = 1.15x

## Slide 36
Amdahl’s Law
Get enhancement E for your new PC
  E.g. floating-point rocket booster
E
  Speeds up some task (e.g. arithmetic) by factor SE
  F is fraction of program that uses this ”task”
1-F | F
1-F | F / SE
Execution Time:
Speedup:
T0 (no E)
TE (with E)
no speedup
speedup section
Speedup = TO / TE = 1 / ((1-F) + F/SE)

## Slide 37
Big Idea: Amdahl’s Law
Part not sped up
Part sped up
Example: The execution time of half of a program can be accelerated by a factor of 2. What is the program speed-up overall?
Speedup = TO / TE = 1 / ((1-F) + F/SE)
TO / TE = 1 / ((1-F) + F/SE) = 1/((1- 0.5)+0.5/2) = 1.33 << 2

## Slide 38
Maximum “Achievable” Speed-Up
Question: What is a reasonable # of parallel processors to speed up an algorithm with F = 95%? (i.e. 19/20th can be sped up)
a) Maximum speedup: Smax = 1/(1-0.95) = 20
but needs SE=∞!
Reasonable “engineering” compromise:
Equal time in sequential and parallel code: (1-F) = F/SE
SE = F/(1-F) = 0.95/0.05 = 20
S = 1/(0.05+0.05) = 10
Speedup = 1 / ((1-F) + F/SE)
(SE->∞) = 1/(1-F)

## Slide 39
Maximum “Achievable” Speed-Up
If the portion of the program that can be parallelized is small, then the speedup is limited
In this region, the sequential portion limits the performance
500 processors
for 19x
20 processors
for 10x

## Slide 40
Strong and Weak Scaling
To get good speedup on a parallel processor while keeping the problem size fixed is harder than getting good speedup by increasing the size of the problem.
  Strong scaling: when speedup can be achieved on a parallel processor without increasing the size of the problem
  Weak scaling: when speedup is achieved on a parallel processor by increasing the size of the problem proportionally to the increase in the number of processors
Load balancing is another important factor: every processor doing same amount of work
  Just one unit with twice the load of others cuts speedup almost in half

## Slide 41
Peer Instruction
Suppose a program spends 80% of its time in a square-root routine. How much must you speedup square root to make the program run 5 times faster?
Speedup = 1 / ((1-F) + F/SE)
RED: 5
GREEN: 20
ORANGE: 500
YELLOW: None of above

## Slide 42
Amdahl’s Law applied to dgemm
Measured dgemm performance
  Peak 5.5 GFLOPS
  Large matrices 3.6 GFLOPS
  Processor 24.8 GFLOPS
Why are we not getting (close to) 25 GFLOPS?
  Something else (not floating-point ALU) is limiting performance!
  But what? Possible culprits:
    Cache
    Hazards
    Let’s look at both!

## Slide 43
Pipeline Hazards – dgemm

## Slide 44
Loop Unrolling
Compiler does the unrolling
How do you verify that the generated code is actually unrolled?
4 registers

## Slide 45
Performance
N | Gflops |  | 
 | scalar | avx | unroll
32 | 1.30 | 4.56 | 12.95
160 | 1.30 | 5.47 | 19.70
480 | 1.32 | 5.27 | 14.50
960 | 0.91 | 3.64 | 6.91
?
WOW!

## Slide 46
FPU versus Memory Access
How many floating-point operations does matrix multiply take?
  F = 2 x N3 (N3 multiplies, N3 adds)
How many memory load/stores?
  M = 3 x N2 (for A, B, C)
Many more floating-point operations than memory accesses
  q = F/M = 2/3 * N
  Good, since arithmetic is faster than memory access
  Let’s check the code …

## Slide 47
But memory is accessed repeatedly
q = F/M = 1! (2 loads and 2 floating-point operations)
Inner loop:

## Slide 48
Typical Memory Hierarchy
Where are the operands (A, B, C) stored?
What happens as N increases?
Idea: arrange that most accesses are to fast cache!
Second-Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s-1000 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)

## Slide 49
Sub-Matrix Multiplication or: Beating Amdahl’s Law
Blocking:
  Rearrange code to use values loaded in cache many times
  Only “few” accesses to slow main memory (DRAM) per floating point operation
  → throughput limited by FP hardware and cache, not slow DRAM
  P&H, RISC-V edition p. 465

## Slide 50
Memory Access Blocking

## Slide 51
Performance
N | Gflops |  |  | 
 | scalar | avx | unroll | blocking
32 | 1.30 | 4.56 | 12.95 | 13.80
160 | 1.30 | 5.47 | 19.70 | 21.79
480 | 1.32 | 5.27 | 14.50 | 20.17
960 | 0.91 | 3.64 | 6.91 | 15.82

## Slide 52
And in Conclusion, …
Approaches to Parallelism
  SISD, SIMD, MIMD (next lecture)
SIMD
  One instruction operates on multiple operands simultaneously
Example: matrix multiplication
  Floating point heavy → exploit Moore’s law to make fast
Amdahl’s Law:
  Serial sections limit speedup
  Cache
    Blocking
  Hazards
    Loop unrolling