## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (百人计划研究员)
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Great Idea #1: Abstraction
(Levels of Representation/Interpretation)
lw t0, t2, 0
lw t1, t2, 4
sw t1, t2, 0 sw t0, t2, 4
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Language Program (RISC-V)
Machine Interpretation
0000 | 1001 | 1100 | 0110 | 1010 | 1111 | 0101 | 1000
1010 | 1111 | 0101 | 1000 | 0000 | 1001 | 1100 | 0110
1100 | 0110 | 1010 | 1111 | 0101 | 1000 | 0000 | 1001
0101 | 1000 | 0000 | 1001 | 1100 | 0110 | 1010 | 1111
Architecture Implementation
Logic Circuit Description (Circuit Schematic Diagrams)
temp = v[k]; v[k] = v[k+1]; v[k+1] = temp;
Anything can be represented
as a number, i.e., data or instructions
We are here!

## Slide 3
Switches: Basic Element of Physical Implementations
A
Z
Z  A
A
Z
Close switch (if A is “1” or asserted) and turn on light bulb (Z)
Open switch (if A is “0” or unasserted) and turn off light bulb (Z)
Implementing a simple circuit (arrow shows action if wire changes to “1” or is asserted):
Compose switches into more complex ones (Boolean functions):
AND
Z  A and B
A
B
OR
Z  A or B
A
B

## Slide 4
CMOS Transistors
Three terminals: source, gate, and drain
  Switch action: if voltage on gate terminal is (some amount) higher/lower than source terminal then conducting path established between drain and source terminals (switch is closed)
Gate
Drain
Source
n-channel transitor open when voltage at Gate is low closes when:
voltage(Gate) > voltage (Threshold)
(High resistance when gate voltage Low,
Low resistance when gate voltage High)
p-channel transistor closed when voltage at Gate is low opens when:
voltage(Gate) > voltage (Threshold)
(Low resistance when gate voltage Low,
High resistance when gate voltage High)
Gate
Source
Drain
Gate
Source
Drain
Note circle symbol to indicate “NOT” or “complement”

## Slide 5
MOS Networks
1v
X
Y
0 volts
(gnd)
x
y
1 volt
(Vdd)
0v
what is the relationship between x and y?
p-channel transistor closed when voltage at Gate is low opens when:
voltage(Gate) > voltage (Threshold)
n-channel transitor open when voltage at Gate is low closes when:
voltage(Gate) > voltage (Threshold)
Called an inverter or not gate

## Slide 6
Two Input Networks
x
y
z
0 volts
1 volt
0 volt
1 volt
0 volts
0 volts
1 volt
1 volt
what is the relationship between x, y and z?
1v
X
Y
0v
Z
1v
X
Y
0v
Z
x
y
z
0 volts
1 volt
0 volt
1 volt
0 volts
0 volts
1 volt
1 volt

## Slide 7
Truth Tables List outputs for all possible inputs
F
Y
A
B
C
D

## Slide 8
A Conceptual RISC-V Datapath

## Slide 9
Logisim
Free schematic capture/logic simulation program in Java
  “A graphical tool for designing and simulating logic circuits”
  Search and download version 2.7.1, online tutorial
  ozark.hendrix.edu/~burch/logisim/
Drawing interface based on toolbar
  Color-coded wires aid in simulating and debugging a circuit
  Wiring tool draws horizontal and vertical wires, automatically connecting to components and to other wires.
Circuit layouts used as "subcircuits" of other circuits, allowing hierarchical circuit design
Included circuit components: inputs and outputs, gates, multiplexers, arithmetic circuits, flip-flops, RAM memory

## Slide 10
Logisim Wires
Blue wires: value at that point is "unknown”
Gray wires: not connected to anything
OK when in process of building a circuit
When finished => wires not be blue or gray
If connected, all wires should be green
  Bright green a 1
  Dark green a 0

## Slide 11
Common Mistakes in Logisim
Connecting wires together
Using input for output
Connecting to edge without connecting to actual input
  Unexpected direction of input

## Slide 12
Types of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
Combinational Logic (CL) circuits
  Output is a function of the inputs only, not the history of its execution
  E.g., circuits to add A, B (ALUs)
  Last lecture was comninational logic
Sequential Logic (SL)
  Circuits that “remember” or store information
  aka “State Elements”
  E.g., memories and registers (Registers)
  Rest of today’s lecture is sequential logic

## Slide 13
Program Counter: First Design
Program Counter “PC”
  Instruction address
  Next PC: add 4 to current value
  Let’s try …
Something is not quite right:
  PC and PC+4 simutaneously on same wire???
PC + 4

## Slide 14
Fix
Memory element breaks the feedback loop
How does it work?

## Slide 15
(Positive) Edge Triggered Flip-Flop
D
Q
clk
Time
Clock “clk”
RS latch operates on input levels
D FF operates on (clock) edges

## Slide 16
Program Counter: Improved Design
Next PC
Current PC

## Slide 17
Clock
Clock frequency fs | Period tcycle = 1/fs
CPU 2.5 GHz | 400 ps
Drum/heartbeat, 1Hz | 1 s
fs = 1/ tcycle

## Slide 18
Maximum Clock Speed
How fast can the PC circuit operate?
  I.e. what is the maximum clock frequency?
Let’s look at the timing requirements of each part
  Let’s start with the flip-flop

## Slide 19
Flip-Flop Timing

## Slide 20
Flip-Flop Timing
Time | Description
tsetup | time during which D must not change before positive clock edge
thold | time during which D must not change after positive clock edge
tclk-to-Q | delay after positive clock edge after which D appears at Q output

## Slide 21
Maximum Clock Speed
Combinatorial
Logic
(CL)
Register
(flip-flops)
Optional Feedback
Output
Input
Clock
CL
tCL

## Slide 22
Maximum PC Clock Speed
Minimum cycle time:
Maximum clock rate:
Example: tsetup ≥ 15ps, tadd = 75ps, tclk-toQ ≥ 10ps
tmin ≥ 100ps
fclk-max ≤ 10GHz

## Slide 23
Example: Serial Communication
Wifi sends data “1 bit at a time”
How do we know where a byte “starts”?
Send “preamble …”
  E.g. 3 one’s in a row

## Slide 24
FSM to Detect 3 One’s
* FSM = Finite State Machine
State transitions are controlled by the clock: on each clock cycle the FSM
  checks the inputs,
  transitions to a new state, and
  produces a new output …
State transition diagram:
FSM to detect the occurrence of 3 consecutive 1’s in the input.
Input/output
S0: idle
S1: detected 1
S2: detected 11

## Slide 25
FSM Combinatorial Logic
Truth Table
State Encoding
State | Code
S0 | 00
S1 | 01
S2 | 10
unused | 11
PS | Input | NS | Output
XX | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 1 | 10 | 0
10 | 1 | 00 | 1
11 | X | 00 | 0

## Slide 26
Hardware Implementation of FSM

## Slide 27
Finite State Machines (FSM) - Summary
Describe computation over time
Represent FSM with “state transition diagram”
Start at given state and input, follow some edge to next (or same) state
With combinational logic and registers, any FSM can be implemented in hardware
state transition diagram

## Slide 28
Conceptual RISC-V Datapath

## Slide 29
Data Multiplexer (e.g., 2-to-1 x n-bit-wide)

## Slide 30
How Do We Build a 1-bit-Wide Mux (in Logisim)?

## Slide 31
4-to-1 Multiplexer
How many rows in Truth Table?

## Slide 32
Alternative Hierarchical Approach (in Logisim)

## Slide 33
Arithmetic and Logic Unit
Most processors contain a special logic block called “Arithmetic and Logic Unit” (ALU)
We’ll show you an easy one that does ADD, SUB, bitwise AND, bitwise OR

## Slide 34
Simple ALU

## Slide 35
Adder/Subtractor: One-bit adder Least Significant Bit
Half Adder

## Slide 36
Adder/Subtractor: One-bit adder (1/2) …
Full Adder

## Slide 37
Adder/Subtractor: One-bit Adder (2/2) …

## Slide 38
N x 1-bit Adders  1 N-bit Adder
+
+
+
b0
Connect Carry Out i-1 to Carry in i:

## Slide 39
Twos Complement Adder/Subtractor

## Slide 40
Critical Path
When setting clock period in synchronous systems, must allow for worst case
Path through combinational logic that is worst case called “critical path”
  Can be estimated by number of “gate delays”: Number of gates must go through in worst case
Idea: Doesn’t matter if speedup other paths if don’t improve the critical path
What might critical path of ALU?

## Slide 41
Processor Design Process
Five steps to design a processor:
  Analyze instruction set  datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 42
The RISC-V Lite Subset
ADD and SUB
  add rd,rs1,rs2
  sub rd,rs1,rs2
OR Immediate:
  ori rd,rs1,imm12
LOAD and STORE Word
  lw rd,rs1,imm12
  sw rs2,rs1,imm12
BRANCH:
  beq rs1,rs2,imm12

## Slide 43
Register Transfer Language (RTL)
RTL gives the meaning of the instructions
{op , rs1 , rs2 , rd , funct3}  MEM[ PC ]
{op , rs1 , rs2 , Imm12}  MEM[ PC ]
All start by fetching the instruction
Inst Register Transfers
ADD R[rd]  R[rs1] + R[rs2]; PC  PC + 4
SUB R[rd]  R[rs1] – R[rs2]; PC  PC + 4
ORI R[rd]  R[rs1] | sign_ext(Imm12); PC  PC + 4
LW R[rd]  MEM[ R[rs1] + sign_ext(Imm12)]; PC  PC + 4
SW MEM[ R[rs1] + sign_ext(Imm12) ]  R[rs2]; PC  PC + 4
BEQ if ( R[rs] == R[rt] ) then PC  PC + (sign_ext(Imm12) || 0) else PC  PC + 4

## Slide 44
Step 1: Requirements of the Instruction Set
Memory (MEM)
  Instructions & data (will use one for each: really caches)
Registers (R: 32 x 32)
  Read rs1
  Read rs2
  Write rd
PC
Sign Extender
Add/Sub/OR unit for operation on register(s) or sign extended immediate
Add 4 (or maybe sign extended immediate) to PC
Compare if registers equal?

## Slide 45
Generic Steps of Datapath
instruction
memory
+4
rs2
rs1
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux

## Slide 46
Step 2: Components of the Datapath
Combinational Elements
State Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder
Zero

## Slide 47
ALU Needs for RISC-V Lite + Rest of RISC-V
Addition, subtraction, logical OR, ==:
  ADD R[rd] = R[rs1] + R[rs2]; ...
  SUB R[rd] = R[rs1] – R[rs2]; ...
  ORI R[rt] = R[rs1] | sign_ext(Imm12)...
  BEQ if ( R[rs] == R[rt] )...
Test to see if output == 0 for any ALU operation gives == test. How?
P&H Ch. 4 also adds AND, 64 bit LD/SD instructions
ALU from Appendix A, Section A.5

## Slide 48
Storage Element: Idealized Memory
Memory (idealized)
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  Address selects the word to put on Data Out
  Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid → Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address

## Slide 49
Storage Element: Register (Building Block)
Similar to D Flip Flop except
  N-bit input and output
  Write Enable input
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on rising edge of clock
clk
Data In
Write Enable
N
N
Data Out

## Slide 50
Storage Element: Register File
Register File consists of 32 registers:
  Two 32-bit output busses:
busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid → busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 51
Step 3: Assemble DataPath Meeting Requirements
Register Transfer Requirements → Datapath Assembly
Instruction Fetch
Read Operands and Execute Operation
Common RTL operations
  Fetch the Instruction: mem[PC]
  Update the program counter:
    Sequential Code: PC ← PC + 4
    Branch and Jump: PC ← “something else”
32
Instruction Word
Address
Instruction
Memory
PC
clk
Next Address
Logic

## Slide 52
Step 3: Add & Subtract
R[rd] = R[rs] op R[rt] (addu rd,rs,rt)
  Ra, Rb, and Rw come from instruction’s Rs1, Rs2, and Rd fields
  ALUctr and RegWr: control logic after decoding the instruction
… Already defined the register file & ALU
32
Result
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
ALU
Zero
rs1
rs2
rd

## Slide 53
And in Conclusion, …
State Machines
  Finite State Machines: made from Stateless combinational logic and Stateful “Memory” Logic (aka Registers)
  Clocks synchronize D-FF change (Setup and Hold times important!)
  Pipeline long-delay CL for faster clock cycle - Split the critical path
Use muxes to select among inputs
  S input bits selects 2S inputs
  Each input can be n-bits wide, independent of S
Can implement muxes hierarchically
Arithmetic circuits are a kind of combinational logic
Control
Datapath
Memory
Processor
Input
Output
Five steps to processor design:
  Analyze instruction set → datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  Assemble the control logic
    Formulate Logic Equations
    Design Circuits