## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Great Idea #1: Abstraction
(Levels of Representation/Interpretation)
lw t0, t2, 0
lw t1, t2, 4
sw t1, t2, 0 sw t0, t2, 4
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Language Program (RISC-V)
Machine Interpretation
0000 | 1001 | 1100 | 0110 | 1010 | 1111 | 0101 | 1000
1010 | 1111 | 0101 | 1000 | 0000 | 1001 | 1100 | 0110
1100 | 0110 | 1010 | 1111 | 0101 | 1000 | 0000 | 1001
0101 | 1000 | 0000 | 1001 | 1100 | 0110 | 1010 | 1111
Architecture Implementation
Logic Circuit Description (Circuit Schematic Diagrams)
temp = v[k]; v[k] = v[k+1]; v[k+1] = temp;
Anything can be represented
as a number, i.e., data or instructions
We are here!

## Slide 3
Instructions interact with each other in pipeline
An instruction in the pipeline may need a resource being used by another instruction in the pipeline  structural hazard
An instruction may depend on something produced by an earlier instruction
  Dependence may be for a data value  data hazard
  Dependence may be for the next instruction’s address  control hazard (branches, exceptions)
Handling hazards generally introduces bubbles into pipeline and reduces ideal CPI > 1

## Slide 4
Review: Three Strategies for Data Hazards
Interlock
  Wait for hazard to clear by holding dependent instruction in issue stage
Bypass
  Resolve hazard earlier by bypassing value as soon as available
Speculate
  Guess on value, correct if wrong

## Slide 5
Interlocking Versus Bypassing
add x1, x3, x5
sub x2, x1, x4
F
add x1, x3, x5
D
F
X
D
F
sub x2, x1, x4
W
M
X
bubble
F
D
W
X
M
W
M
W
W
M
D
X
bubble
M
X
bubble
D
F
Instruction interlocked in decode stage
F
D
X
M
W
add x1, x3, x5
F
D
X
M
W
sub x2, x1, x4
Bypass around ALU with no bubbles

## Slide 6
Fully Bypassed Data Path
Memory
EXecute
Decode
Fetch
Registers
ALU
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
[ Assumes data written to registers in a W cycle is readable in parallel D cycle (dotted line). Extra write data register and bypass paths required if this is not possible. ]

## Slide 7
Register vs. Memory Dependence
Data hazards due to register operands can be determined at the decode stage, but data hazards due to memory operands can be determined only after computing the effective address
Store: M[r1 + disp1] ← r2
Load: r3 ← M[r4 + disp2]
Does (r1 + disp1) = (r4 + disp2) ?

## Slide 8
Complex Pipelining: Motivation
Pipelining becomes complex when we want high performance in the presence of:
Long latency or partially pipelined floating-point units
Memory systems with variable access time
Multiple arithmetic and memory units

## Slide 9
Issues in Complex Pipeline Control
Structural conflicts at the execution stage if some FPU or memory unit is not pipelined and takes more than one cycle
Structural conflicts at the write-back stage due to variable latencies of different functional units
Out-of-order write hazards due to variable latencies of different functional units
How to handle exceptions?
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPRs
FPRs

## Slide 10
Types of Data Hazards
Consider executing a sequence of
rk ← ri op rj
type of instructions
Data-dependence
      r3 ← r1 op r2 Read-after-Write
      r5 ← r3 op r4 (RAW) hazard
Anti-dependence
      r3 ← r1 op r2 Write-after-Read
      r1 ← r4 op r5 (WAR) hazard
Output-dependence
      r3 ← r1 op r2 Write-after-Write
      r3 ← r6 op r7 (WAW) hazard

## Slide 11
Data Hazard Examples
WAW (write after write) - j tries to write an operand before it is written by i. The writes end up being performed in the wrong order, leaving the value written by i rather than the value written by j in the destination.
LW R1, 0(R2) | IF | ID | EX | MEM1 | MEM2 | WB
ADD R1, R2, R3 |  | IF | ID | EX | WB | 
WAR (write after read) - j tries to write a destination before it is read by i , so i incorrectly gets the new value.
SW R1, 0(R2) | IF | ID | EX | MEM1 | MEM2 | WB
ADD R2, R3, R4 |  | IF | ID | EX | WB | 

## Slide 12
Data Hazards: An Example
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
RAW Hazards
WAR Hazards
WAW Hazards

## Slide 13
Recap: Complex In-Order Pipeline
Delay writeback so all operations have same latency to W stage
  Write ports never oversubscribed (one inst. in & one inst. out every cycle)
  Stall pipeline on long latency operations, e.g., divides, cache misses
  Handle exceptions in-order at commit point
Commit Point
PC
Inst. Mem
D
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider
How to prevent increased writeback latency from slowing down single-cycle integer operations?
Bypassing

## Slide 14
Complex Pipeline
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s
Can we solve write hazards without equalizing all pipeline depths and without bypassing?
OoO

## Slide 15
What is OOO?
OOO execution is a type of processing where the instructions can begin execution as soon as operands are ready
Instructions are issued in order however execution proceeds out of order
Evolution
CDC 6600
IBM 360/91 Tomasulo's algorithm IBM/Motorola PowerPC 601
1993
1964
1966
1995 | Fujitsu/HAL SPARC64, Intel Pentium Pro
1996 | MIPS R10000, AMD K5
1998 2011 | DEC Alpha 21264 Sandy Bridge

## Slide 16
Why Out-­of-­Order?
Great for ...
  tolerating variable latencies
  ﬁnding ILP in code (instruction-­level parallelism)
  complex method for ﬁne-­grain data prefetching
  plays nicely with poor compilers and lazily written code
Downsides
  complicated
  expensive (area & power)
Performance! (and easy to program!)
add r1, r0, r0
Ld r2, M[r10]
sub r3, r2, r13
mul r4, r14, r15

## Slide 17
OoO is widely used in industry
Intel Xeon/i-series (10-100W)
ARM Cortex mobile chips (1W)
Sun/Oracle Niagra UltraSPARC
Intel Atom
Play Station

## Slide 18
Instruction Scheduling
I6
I2
I4
I1
I5
I3
Valid orderings:
in-order I1 I2 I3 I4 I5 I6
out-of-order
out-of-order
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
I2 I1 I3 I4 I5 I6
I1 I2 I3 I5 I4 I6

## Slide 19
When is it Safe to Issue an Instruction?
Suppose a data structure keeps track of all the instructions in all the functional units
The following checks need to be made before the Issue stage can dispatch an instruction
  Is the required function unit available?
  Is the input data available? (RAW?)
  Is it safe to write the destination? (WAR?WAW?)
  Is there a structural conflict at the WB stage?

## Slide 20
A Data Structure for Correct Issues Keeps track of the status of Functional Units
The instruction i at the Issue stage consults this table
  FU available? check the busy column
  RAW? search the dest column for i’s sources
  WAR? search the source columns for i’s destination
  WAW? search the dest column for i’s destination
An entry is added to the table if no hazard is detected;
An entry is removed from the table after Write-Back
Name Busy Op Dest Src1 Src2
  Int
  Mem
  Add1
  Add2
  Add3
  Mult1
  Mult2
  Div

## Slide 21
Simplifying the Data Structure Assuming In-order Issue
Suppose the instruction is not dispatched by the Issue stage if a RAW hazard exists or the required FU is busy, and that operands are latched by functional unit on issue:
Can the dispatched instruction cause a
  WAR hazard ?
  WAW hazard ?
NO: Operands read at issue
YES: Out-of-order completion

## Slide 22
Simplifying the Data Structure ...
No WAR hazard
  →no need to keep src1 and src2
The Issue stage does not dispatch an instruction in case of a WAW hazard
  → a register name can occur at most once in the dest column
WP[reg#] : a bit-vector to record the registers for which writes are pending
  These bits are set by the Issue stage and cleared by the WB stage
  → Each pipeline stage in the FU's must carry the register destination field and a flag to indicate if it is valid

## Slide 23
Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
  (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set by Issue stage and cleared by WB stage
Issue checks the instruction (opcode dest src1 src2)
  against the scoreboard (Busy & WP) to dispatch
  FU available?
  RAW?
  WAR?
  WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 24
Scoreboard Dynamics
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
  Functional Unit Status Registers Reserved
  Int(1) Add(1) Mult(3) Div(4) WB for Writes
t0 I1 f6 f6
t1 I2 f2 f6 f6, f2
t2 f6 f2 f6, f2 I2
t3 I3 f0 f6 f6, f0
t4 f0 f6 f6, f0 I1
t5 I4 f0 f8 f0, f8
t6 f8 f0 f0, f8 I3
t7 I5 f10 f8 f8, f10
t8 f8 f10 f8, f10 I5
t9 f8 f8 I4
t10 I6 f6 f6
t11 f6 f6 I6

## Slide 25
Out-of-order Completion In-order Issue
Latency
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMULT.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
in-order comp 1 2
out-of-order comp 1 2
1 2 3 4 3 5 4 6 5 6
2 3 1 4 3 5 5 4 6 6

## Slide 26
In-Order Issue Limitations: an example
latency
1 | LD | F2, | 34(R2) |  | 1
2 | LD | F4, | 45(R3) |  | long
3 | MULTD | F6, | F4, | F2 | 3
4 | SUBD | F8, | F2, | F2 | 1
5 | DIVD | F4, | F2, | F8 | 4
6 | ADDD | F10, | F6, | F4 | 1
1
2
3
4
5
6
In-order:
1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
In-order issue restriction prevents instruction 4 from being dispatched

## Slide 27
In-Order Issue Limitations: an example
latency
1 | LD | F2, | 34(R2) |  | 1
2 | LD | F4, | 45(R3) |  | long
3 | MULTD | F6, | F4, | F2 | 3
4 | SUBD | F8, | F2, | F2 | 1
5 | DIVD | F4, | F2, | F8 | 4
6 | ADDD | F10, | F6, | F4 | 1
1
2
3
4
5
6
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
Out-of-order: 1 (2,1) 4 4 . . . . 2 3 . . 3 5 . . . 5 6 6
Out-of-order execution did not allow any significant improvement!

## Slide 28
Out-of-Order Issue
Issue stage buffer holds multiple instructions waiting to issue.
Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
  Note: WAR possible again because issue is out-of-order (WAR not possible with in-order issue and latching of input operands at functional unit)
Any instruction in buffer whose RAW hazards are satisfied can be issued (for now, at most one dispatch per cycle). On a write back (WB), new instructions may get enabled.
IF
ID
WB
ALU
Fadd
Issue
Mem
Fmul

## Slide 29
How many Instructions can be in the pipeline
Which features of an ISA limit the number of instructions in the pipeline?
Number of Registers
Which features of a program limit the number of instructions in the pipeline?
Control transfers
Out-of-order dispatch by itself does not provide any significant performance improvement !

## Slide 30
Overcoming the Lack of Register Names
Floating Point pipelines often cannot be kept filled with small number of registers.
  IBM 360 had only 4 Floating Point Registers
Can a microarchitecture use more registers than specified by the ISA without loss of ISA compatibility ?
  Robert Tomasulo of IBM suggested an ingenious solution in 1967 based on on-the-fly register renaming

## Slide 31
Issue Limitations: In-Order and Out-of-Order
latency
1
2
3
4
X
5
6
. . 5 6 6
1 | LD | F2, | 34(R2) |  |  | 1
2 | LD | F4, | 45(R3) |  |  | long
3 | MULTD | F6, | F4, |  | F2 | 3
4 | SUBD | F8, | F2, |  | F2 | 1
5 | DIVD | F4’, | F2, |  | F8 | 4
6 | ADDD | F10, | F6, |  | F4’ | 1
In-order: |  | 1 (2,1) . . . . . |  | . 2 3 4 4 3 5 . |  | 
Out-of-order: |  | 1 (2,1) 4 4 5 . . |  | . 2 (3,5) 3 6 6 |  | 
Any antidependence can be eliminated by renaming. (renaming  additional storage)
Can it be done in hardware?
yes!

## Slide 32
Register Renaming
Decode does register renaming and adds instructions to the issue stage reorder buffer (ROB)
  renaming makes WAR or WAW hazards impossible
Any instruction in ROB whose RAW hazards have been satisfied can be dispatched.
  Out-of-order or dataflow execution
IF
ID
WB
ALU
Fadd
Issue
Mem
Fmul

## Slide 33
Renaming & Out-of-order Issue An example
t1 t2
.
.
.
data / ti
Renaming table Reorder buffer
p data Ins# use exec op p1 src1 p2 src2
F1 F2 F3 F4 F5 F6 F7 F8
LD
F2,
LD F4,
MULTD F6, SUBD F8,
1
2
3
4
5
6
DIVD ADDD
34(R2)
45(R3) F4, F2
F2, F2
F4, F2, F8
F10, F6, F4
When are names in sources replaced by data?
Whenever an FU produces data
When can a name be reused?
Whenever an instruction completes

## Slide 34
Data-Driven Execution
Renaming table & reg file
Reorder buffer
Load Unit
FU
FU
Store Unit
< t, result >
Ins# use exec
op p1 src1
t1 t2
.
.
tn
Replacing the tag by its value is an expensive operation
p2 src2
Instruction template (i.e., tag t) is allocated by the Decode stage, which also stores the tag in the reg file
When an instruction completes, its tag is deallocated

## Slide 35
Reorder Buffer Management
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 36
Renaming & Out-of-order Issue
An example
When are tags in sources
replaced by data?
When can a name be reused?
1 FLD f2, 34(x2)
2 FLD f4, 45(x3)
3 FMULT.D f6, f4, f2
4 FSUB.D f8, f2, f2
5 FDIV.D f4, f2, f8
6 FADD.D f10, f6, f4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
t3
t4
t5
.
.
data / ti
p data
f1
f2
f3
f4
f5
f6
f7
f8
Whenever an FU produces data
Whenever an instruction completes
t1
1 1 0 LD
t2
2 1 0 LD
5 1 0 DIV 1 v1 0 t4
4 1 0 SUB 1 v1 1 v1
t4
3 1 0 MUL 0 t2 1 v1
t3
t5
v1
1 1 1 LD
1 0
4 1 1 SUB 1 v1 1 v1
4 0
v4
5 1 0 DIV 1 v1 1 v4
2 1 1 LD
2 0
3 1 0 MUL 1 v2 1 v1

## Slide 37
Data Movement in Data-in-ROB Design
ROB
Architectural Register File
Read operands during decode
Read operands at issue
Functional Units
Read results for commit
Bypass newer values at dispatch
Result Data
Write results at completion
Write results at commit
Source Operands
Write sources in dispatch

## Slide 38
IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 39
Effectiveness?
Renaming and Out-of-order execution was first implemented in 1969 in IBM 360/91 but did not show up in the subsequent models until mid- Nineties.
Why ?
Reasons
Exceptions not precise!
Effective on a very small class of programs
Memory latency a much bigger problem
One more problem needed to be solved
Control transfers

## Slide 40
Out-of-Order Fades into Background
Out-of-order processing implemented commercially in 1960s, but disappeared again until 1990s as two major problems had to be solved:
Precise traps
  Imprecise traps complicate debugging and OS code
  Note, precise interrupts are relatively easy to provide
Branch prediction
  Amount of exploitable instruction-level parallelism (ILP) limited by control hazards
Also, simpler machine designs in new technology beat complicated machines in old technology
  Big advantage to fit processor & caches on one chip
  Microprocessors had era of 1%/week performance scaling

## Slide 41
Precise Interrupts
It must appear as if an interrupt is taken between two instructions (say Ii and Ii+1)
  the effect of all instructions up to and including Ii is totally complete
  no effect of any instruction after Ii has taken place
The interrupt handler either aborts the program or restarts it at Ii+1.

## Slide 42
Effect on Interrupts
Out-of-order Completion
I1 I2 I3 I4 I5 I6
f4
f4 f2 f6 f2
out-of-order comp
restore f2
DIVD f6, f6,
LD f2, 45(r3)
MULTD f0, f2,
DIVD f8, f6,
SUBD f10, f0,
ADDD f6, f8,
1 2 2 3 1 4 3 5 5 4 6 6
restore f10
Consider interrupts
Precise interrupts are difficult to implement at high speed
- want to start execution of later instructions before exception checks finished on earlier instructions

## Slide 43
Exception Handling
(In-Order Five-Stage Pipeline)
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage
Commit
Asynchronous Interrupts
Exc
D
PC D
PC
Inst. Mem
D
Decode
E
M
Data
Mem
W
+
Exc
E
PC E
Exc
M
PC M
Cause
EPC
Illegal Opcode
Overflow
Data Addr Except
Kill
W iteback
r
Point
Kill D Stage
Kill F Stage
Kill E Stage
PC Address Exceptions
Select Handler PC

## Slide 44
Phases of Instruction Execution
Fetch: Instruction bits retrieved from instruction cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural State
Execute: Instructions and operands issued to functional units. When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue buffer
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation”), or takes precise trap/interrupt.
PC
Commit
Decode/Rename

## Slide 45
In-Order Commit for Precise Exceptions
In-order Out-of-order
In-order
Fetch Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
Exception?
Inject handler PC
Instructions fetched and decoded into instruction reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile & memory, is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)

## Slide 46
Extensions for Precise Exceptions
Inst# use exec op p1 src1 p2 src2 pd dest data cause
ptr2 next to commit
ptr1 next available
Reorder buffer
add <pd, dest, data, cause> fields in the instruction template
commit instructions to reg file and memory in program order  buffers can be maintained circularly
on exception, clear reorder buffer by resetting ptr1=ptr2
(stores must wait for commit before updating memory)

## Slide 47
Rollback and Renaming
(HP PA8000, Pentium Pro, Core2Duo, Nehalem)
Reorder buffer
Register File (now holds only committed state)
Load Unit
FU FU
FU
Store Unit
t1 t2
.
.
tn
Ins#
use
exec
op
p1 src1 p
2 src2
pd dest
data
Commit
< t, result > Register file does not contain renaming tags any more.
How does the decode stage find the tag of a source register?
Search the “dest” field in the reorder buffer

## Slide 48
Renaming Table
Rename Table
Reorder buffer
Register
File
Load Unit
FU FU
FU
Store Unit
t1 t2
.
.
tn
Ins#
use
exec
op
p1 src1 p
2 src2
pd dest
data
Commit
t | v
r1 r2
tag valid bit
< t, result > Renaming table is a cache to speed up register name look up. It needs to be cleared after each exception taken.
When else are valid bits cleared?
Control transfers

## Slide 49
Control-Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
~ Loop length x pipeline width + buffers

## Slide 50
Average Run-Length between Branches
Average dynamic instruction mix from SPEC92:
 | SPECint92 | SPECfp92
ALU | 39 % | 13 %
FPU Add |  | 20 %
FPU Mult |  | 13 %
load | 26 % | 23 %
store | 9 % | 9 %
branch | 16 % | 8 %
other | 10 % | 12 %
SPECint92: SPECfp92:
compress, eqntott, espresso, gcc , li doduc, ear, hydro2d, mdijdp2, su2cor
What is the average run length between branches

## Slide 51
Reducing Control-Flow Penalty
Software solutions
  Eliminate branches - loop unrolling
    Increases the run length
  Reduce resolution time - instruction scheduling
    Compute the branch condition as early as possible (of limited value because branches often in critical path through code)
Hardware solutions
  Find something else to do (delay slots)
    Replaces pipeline bubbles with useful work (requires software cooperation) – quickly see diminishing returns
  Speculate, i.e., branch prediction
    Speculative execution of instructions beyond the branch
    Many advances in accuracy, widely used

## Slide 52
Branch Prediction
Motivation:
  Branch penalties limit performance of deeply pipelined processors
  Modern branch predictors have high accuracy
  (>95%) and can reduce branch penalties significantly
Required hardware support:
  Prediction structures:
    Branch history tables, branch target buffers, etc.
Mispredict recovery mechanisms:
  Keep result computation separate from commit
  Kill instructions following branch in pipeline
  Restore state to that following branch

## Slide 53
Importance of Branch Prediction
Consider 4-way superscalar with 8 pipeline stages from fetch to dispatch, and 80-entry ROB, and 3 cycles from issue to branch resolution
On a mispredict, could throw away 8*4+(80-1)=111 instructions
Improving from 90% to 95% prediction accuracy, removes 50% of branch mispredicts
  If 1/6 instructions are branches, then move from 60 instructions between mispredicts, to 120 instructions between mispredicts

## Slide 54
Static Branch Prediction
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64 typically reported as ~80% accurate
backward
90%
forward
50%

## Slide 55
Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 56
One-Bit Branch History Predictor
For each branch, remember last way branch went
Has problem with loop-closing backward branches, as two mispredicts occur on every loop execution
  first iteration predicts loop backwards branch not-taken (loop was exited last time)
  last iteration predicts loop backwards branch taken (loop continued last time)

## Slide 57
Branch Prediction Bits
Assume 2 BP bits per instruction
Change the prediction after two consecutive mistakes!
¬take
wrong
taken
¬ taken
taken
taken
taken
¬take
right
take
right
take
wrong
¬ taken
¬ taken
¬ taken
BP state:
(predict take/¬take) x (last prediction right/wrong)

## Slide 58
Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 59
Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition false, second condition also false

## Slide 60
Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 61
Speculating Both Directions?
An alternative to branch prediction is to execute both directions of a branch speculatively
  resource requirement is proportional to the number of concurrent speculative executions
  only half the resources engage in useful work when both directions of a branch are executed speculatively
  branch prediction takes less resources than speculative execution of both paths
With accurate branch prediction, it is more cost effective to dedicate all resources to the predicted direction!

## Slide 62
Limitations of BHTs
Only predicts branch direction. Therefore, cannot redirect fetch stream until after branch target is determined.
UltraSPARC-III fetch pipeline
Correctly predicted
taken branch penalty
Jump Register penalty
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
Remainder of execute pipeline
(+ another 6 stages)

## Slide 63
Branch Target Buffer (BTB)
Keep both the branch PC and target PC in the BTB
PC+4 is fetched if match fails
Only taken branches and jumps held in BTB
Next PC determined before branch fetched and decoded
2k-entry direct-mapped BTB
(can also be associative)
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 64
Combining BTB and BHT
BTB entries are considerably more expensive than BHT, but can redirect fetches at earlier stage in pipeline and can accelerate indirect branches (JR)
BHT can hold many more entries and is more accurate
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
BTB
BHT
BHT in later pipeline stage corrects when BTB misses a predicted taken branch
BTB/BHT only updated after branch resolves in E stage

## Slide 65
Uses of Jump Register (JR)
Switch statements (jump to address of matching case)
Dynamic function call (jump to run-time function address)
Subroutine returns (jump to return address)
How well does BTB work for each of these cases?
BTB works well if same case used repeatedly
BTB works well if same function usually called, (e.g., in C++ programming, when objects have same type in virtual function call)
BTB works well if usually return to the same place
 Often one function called from many distinct call sites!

## Slide 66
Subroutine Return Stack
Small structure to accelerate JR for subroutine returns, typically much more accurate than BTBs.
&fb()
&fc()
Push call address when function call executed
Pop return address when subroutine return decoded
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
&fd()
k entries
(typically k=8-16)

## Slide 67
Return Stack in Pipeline
How to use return stack (RS) in deep fetch pipeline?
Only know if subroutine call/return at decode
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
RS
RS Push/Pop after decode gives large bubble in fetch stream.
Return Stack prediction checked

## Slide 68
Return Stack in Pipeline
Can remember whether PC is subroutine call/return using BTB-like structure
Instead of target-PC, just store push/pop bit
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
RS
Push/Pop before instructions decoded!
Return Stack prediction checked

## Slide 69
In-Order vs. Out-of-Order Branch Prediction
Both styles of machine can use same branch predictors in front-end fetch pipeline, and both can execute multiple instructions per cycle
Common to have 10-30 pipeline stages in either style of design
Speculative fetch but not speculative execution - branch resolves before later instructions complete
Completed values held in bypass network until commit
Speculative execution, with branches resolved after later instructions complete
Completed values held in rename registers in ROB or unified physical register file until commit
Fetch
Decode
Execute
Commit
In-Order Issue
Out-of-Order Issue
Fetch
Decode
Execute
Commit
ROB
Br. Pred.
Resolve
Br. Pred.
Resolve
In-Order
In-Order
In-Order
Out-of-Order

## Slide 70
InO vs. OoO Mispredict Recovery
In-order execution?
  Design so no instruction issued after branch can write-back before branch resolves
  Kill all instructions in pipeline behind mispredicted branch
Out-of-order execution?
  Multiple instructions following branch in program order can complete before branch resolves
  A simple solution would be to handle like precise traps
    Problem?

## Slide 71
Branch Misprediction in Pipeline
Can have multiple unresolved branches in ROB
Can resolve branches out-of-order by killing all the instructions in ROB that follow a mispredicted branch
MIPS R10K uses four mask bits to tag instructions that are dependent on up to four speculative branches
Mask bits cleared as branch resolves, and reused for next branch
Fetch
Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
PC
Inject correct PC
Branch
Prediction
Branch
Resolution
Complete

## Slide 72
Rename Table Recovery
Have to quickly recover rename table on branch mispredicts
MIPS R10K only has four snapshots for each of four outstanding speculative branches
Alpha 21264 has 80 snapshots, one per ROB instruction

## Slide 73
Mispredict Recovery
t
v
t
v
t
v
Register File
Reorder
Buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
r1
t
v
r2
Rename
Snapshots
Ptr2 next to commit
Ptr1 next available
rollback next available
Take snapshot of register rename table at each predicted branch, recover earlier snapshot if branch mispredicted

## Slide 74
OoO Design Choices
Where are reservation stations?
  Part of reorder buffer, or in separate issue window?
  Distributed by functional units, or centralized?
How is register renaming performed?
  Tags and data held in reservation stations, with separate architectural register file
  Tags only in reservation stations, data held in unified physical register file

## Slide 75
Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy/Ivy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 76
Lifetime of Physical Registers
Physical regfile holds committed and speculative values
Physical registers decoupled from ROB entries (no data in ROB)
ld x1, (x3)
addi x3, x1, #4
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x11)
ld P1, (Px)
addi P2, P1, #4
sub P3, Py, Pz
add P4, P2, P3
ld P5, (P1)
add P6, P5, P4
sd P6, (P1)
ld P7, (Pw)
Rename
When can we reuse a physical register?
When next writer of same architectural register commits

## Slide 77
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
ROB
Rename Table
Physical Regs
Free List
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<x1>
P8
p

## Slide 78
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8

## Slide 79
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1

## Slide 80
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3

## Slide 81
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2

## Slide 82
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4

## Slide 83
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 x1 P0
x addi P0 x3 P1
x sub p P6 p P5 x6 P3
x ld p P7 x1 P0
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x

## Slide 84
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 x6 P3
x addi P0 x3 P1
x addi P0 x3 P1
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x
p
p
<x3>
P7

## Slide 85
Repairing Rename at Traps
MIPS R10K rename table is repaired by unrenaming instructions in reverse order using the PRd/LPRd fields
Alpha 21264 had similar physical register file scheme, but kept complete rename table snapshots for each instruction in ROB (80 snapshots total)
  Flash copy all bits from snapshot to active table in one cycle

## Slide 86
Pipeline Design with Physical Regfile
Fetch
Decode & Rename
Reorder Buffer
PC
Branch
Prediction
Commit
Branch
Resolution
Branch
Unit
ALU
MEM
Store Buffer
D$
Execute
In-Order
In-Order
Out-of-Order
Physical Reg. File
kill
kill
kill
kill

## Slide 87
Superscalar Register Renaming
During decode, instructions allocated new physical destination register
Source operands renamed to physical register with newest value
Execution unit only sees physical register numbers
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Does this work?
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports

## Slide 88
Superscalar Register Renaming
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports
=?
=?
Must check for RAW hazards between instructions issuing in same cycle. Can be done in parallel with rename lookup.
MIPS R10K renames 4 serially-RAW-dependent insts/cycle

## Slide 89
Separate Issue Window from ROB
Reorder buffer used to hold exception information for commit.
The instruction window holds instructions that have been decoded and renamed but not issued into execution. Has register tags and presence bits, and pointer to ROB entry.
op
p1
PR1
p2
PR2
PRd
use
ex
ROB#
ROB is usually several times larger than instruction window – why?
Rd
LPRd
PC
Except?
Ptr2 next to commit
Ptr1 next available
Done?
Instructions that committed are not in the instruction window any more

## Slide 90
Separating Completion from Commit
Re-order buffer holds register results from completion until commit
  Entries allocated in program order during decode
  Buffers completed values and exception state until in-order commit point
  Completed values can be used by dependents before committed (bypassing)
  Each entry holds program counter, instruction type, destination register specifier and value if any, and exception status (info often compressed to save hardware)
Memory reordering needs special data structures
  Speculative store address and data buffers
  Speculative load address and data buffers

## Slide 91
Reorder Buffer Holds Active Instructions (Decoded but not Committed)
(Older instructions)
(Newer instructions)
Cycle t
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
Commit
Fetch
Cycle t + 1
Execute
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
ROB contents

## Slide 92
Issue Timing
i1 | Add R1,R1,#1 | Issue1 | Execute1 |  | 
i2 | Sub R1,R1,#1 |  |  | Issue2 | Execute2
How can we issue earlier?
Using knowledge of execution latency (bypass)
What makes this schedule fail?
If execution latency wasn’t as expected
i1 | Add R1,R1,#1 | Issue1 | Execute1 |  | 
i2 | Sub R1,R1,#1 |  | Issue2 | Execute2 | 

## Slide 93
Issue Queue with latency prediction
Fixed latency: latency included in queue entry (‘bypassed’)
Predicted latency: latency included in queue entry (speculated)
Variable latency: wait for completion signal (stall)
Issue Queue (Reorder buffer)
ptr2
next to
commit
ptr1
next
available
Inst# use exec op p1 lat1 src1 p2 lat2 src2 dest
BEQZ
Speculative Instructions

## Slide 94
Improving Instruction Fetch
Performance of speculative out-of-order machines often limited by instruction fetch bandwidth
  speculative execution can fetch 2-3x more instructions than are committed
  mispredict penalties dominated by time to refill instruction window
  taken branches are particularly troublesome

## Slide 95
Increasing Taken Branch Bandwidth (Alpha 21264 I-Cache)
Fold 2-way tags and BTB into predicted next block
Take tag checks, inst. decode, branch predict out of loop
Raw RAM speed on critical loop (1 cycle at ~1 GHz)
2-bit hysteresis counter per block prevents overtraining
Cached Instructions
Line Predict
Way Predict
Tag
Way
0
Tag
Way
1
=?
=?
fast fetch path
PC Generation
PC
Branch Prediction
Instruction Decode
Validity Checks
4 insts
Hit/Miss/Way

## Slide 96
Tournament Branch Predictor (Alpha 21264)
Choice predictor learns whether best to use local or global branch history in predicting next branch
Global history is speculatively updated but restored on mispredict
Claim 90-100% success on range of applications
Local history table (1,024x10b)
PC
Local prediction (1,024x3b)
Global Prediction (4,096x2b)
Choice Prediction (4,096x2b)
Global History (12b)
Prediction

## Slide 97
Taken Branch Limit
Integer codes have a taken branch every 6-9 instructions
To avoid fetch bottleneck, must execute multiple taken branches per cycle when increasing performance
This implies:
  predicting multiple branches per cycle
  fetching multiple non-contiguous blocks per cycle

## Slide 98
Branch Address Cache (Yeh, Marr, Patt)
PC
k
Entry PC
=
match
Valid
valid
predicted
target#1
target #1
len
len#1
predicted
target#2
target #2
Extend BTB to return multiple branch predictions per cycle

## Slide 99
Fetching Multiple Basic Blocks
Requires either
  multiported cache: expensive
  interleaving: bank conflicts will occur
Merging multiple blocks to feed to decoders adds latency, increasing mispredict penalty and reducing branch throughput

## Slide 100
Trace Cache
Key Idea: Pack multiple non-contiguous basic blocks into one contiguous trace cache line
Single fetch brings in multiple basic blocks
Trace cache indexed by start address and next n branch predictions
Used in Intel Pentium-4 processor to hold decoded uops
BR
BR
BR
BR
BR
BR

## Slide 101
Load-Store Queue Design
After control hazards, data hazards through memory are probably next most important bottleneck to superscalar performance
Modern superscalars use very sophisticated load-store reordering techniques to reduce effective memory latency by allowing loads to be speculatively issued

## Slide 102
Speculative Store Buffer
Just like register updates, stores should not modify the memory until after the instruction is committed. A speculative store buffer is a structure introduced to hold speculative store data.
During decode, store buffer slot allocated in program order
Stores split into “store address” and “store data” micro-operations
“Store address” execution writes tag
“Store data” execution writes data
Store commits when oldest instruction and both address and data available:
  clear speculative bit and eventually move data to cache
On store abort:
  clear valid bit
Data
Tags
Store Commit Path
Speculative Store Buffer
L1 Data Cache
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Store Address
Store Data

## Slide 103
Load bypass from speculative store buffer
If data in both store buffer and cache, which should we use?
Speculative store buffer
If same address in store buffer twice, which should we use?
Youngest store older than load
Data
Load Address
Tags
Speculative Store Buffer
L1 Data Cache
Load Data
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V

## Slide 104
Memory Dependencies
sd x1, (x2)
ld x3, (x4)
When can we execute the load?

## Slide 105
In-Order Memory Queue
Execute all loads and stores in program order
  => Load and store cannot leave ROB for execution until all previous loads and stores have completed execution
Can still execute loads and stores speculatively, and out-of-order with respect to other instructions
Need a structure to handle memory ordering…

## Slide 106
Conservative O-o-O Load Execution
sd x1, (x2)
ld x3, (x4)
Can execute load before store, if addresses known and x4 != x2
Each load address compared with addresses of all previous uncommitted stores
  can use partial conservative check i.e., bottom 12 bits of address, to save hardware
Don’t execute load if any previous store address not known
(MIPS R10K, 16-entry address queue)

## Slide 107
Address Speculation
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2
Execute load before store address known
Need to hold all completed but uncommitted load/store addresses in program order
If subsequently find x4==x2, squash load and all following instructions
=> Large penalty for inaccurate address speculation

## Slide 108
Memory Dependence Prediction (Alpha 21264)
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2 and execute load before store
If later find x4==x2, squash load and all following instructions, but mark load instruction as store-wait
Subsequent executions of the same load instruction will wait for all previous stores to complete
Periodically clear store-wait bits

## Slide 109
Instruction Flow in Unified Physical Register File Pipeline
Fetch
  Get instruction bits from current guess at PC, place in fetch buffer
  Update PC using sequential address or branch predictor (BTB)
Decode/Rename
  Take instruction from fetch buffer
  Allocate resources to execute instruction:
    Destination physical register, if instruction writes a register
    Entry in reorder buffer to provide in-order commit
    Entry in issue window to wait for execution
    Entry in memory buffer, if load or store
  Decode will stall if resources not available
  Rename source and destination registers
  Check source registers for readiness
  Insert instruction into issue window+reorder buffer+memory buffer

## Slide 110
Memory Instructions
Split store instruction into two pieces during decode:
  Address calculation, store-address
  Data movement, store-data
Allocate space in program order in memory buffers during decode
  Store instructions:
    Store-address calculates address and places in store buffer
    Store-data copies store value into store buffer
    Store-address and store-data execute independently out of issue window
    Stores only commit to data cache at commit point
Load instructions:
  Load address calculation executes from window
  Load with completed effective address searches memory buffer
  Load instruction may have to wait in memory buffer for earlier store ops to resolve

## Slide 111
Issue Stage
Writebacks from completion phase “wakeup” some instructions by causing their source operands to become ready in issue window
  In more speculative machines, might wake up waiting loads in memory buffer
Need to “select” some instructions for issue
  Arbiter picks a subset of ready instructions for execution
  Example policies: random, lower-first, oldest-first, critical-first
Instructions read out from issue window and sent to execution

## Slide 112
Execute Stage
Read operands from physical register file and/or bypass network from other functional units
Execute on functional unit
Write result value to physical register file (or store buffer if store)
Produce exception status, write to reorder buffer
Free slot in instruction window

## Slide 113
Commit Stage
Read completed instructions in-order from reorder buffer
  (may need to wait for next oldest instruction to complete)
If exception raised
  flush pipeline, jump to exception handler
Otherwise, release resources:
  Free physical register used by last writer to same architectural register
  Free reorder buffer slot
  Free memory reorder buffer slot

## Slide 114
In-Order versus Out-of-Order Phases
Instruction fetch/decode/rename always in-order
  Need to parse ISA sequentially to get correct semantics
  Proposals for speculative OoO instruction fetch, e.g., Multiscalar. Predict control flow and data dependencies across sequential program segments fetched/decoded/executed in parallel, fixup if prediction wrong
Dispatch (place instruction into machine buffers to wait for issue) also always in-order
  Some use “Dispatch” to mean “Issue”, but not in these lectures

## Slide 115
In-Order Versus Out-of-Order Issue
In-order issue:
  Issue stalls on RAW dependencies or structural hazards, or possibly WAR/WAW hazards
  Instruction cannot issue to execution units unless all preceding instructions have issued to execution units
Out-of-order issue:
  Instructions dispatched in program order to reservation stations (or other forms of instruction buffer) to wait for operands to arrive, or other hazards to clear
  While earlier instructions wait in issue buffers, following instructions can be dispatched and issued out-of-order

## Slide 116
In-Order versus Out-of-Order Completion
All but the simplest machines have out-of-order completion, due to different latencies of functional units and desire to bypass values as soon as available
Classic RISC 5-stage integer pipeline just barely has in-order completion
  Load takes two cycles, but following one-cycle integer op completes at same time, not earlier
  Adding pipelined FPU immediately brings OoO completion

## Slide 117
In-Order versus Out-of-Order Commit
In-order commit supports precise traps, standard today
  Some proposals to reduce the cost of in-order commit by retiring some instructions early to compact reorder buffer, but this is just an optimized in-order commit
Out-of-order commit was effectively what early OoO machines implemented (imprecise traps) as completion irrevocably changed machine state
  i.e., complete == commit in these machines

## Slide 118
Open-source Berkeley RISC-V Processors
Sodor Collection
  RV32I -­ Entry, educational, not synthesizable
Rocket-­chip SoC generator
Z-scale
  RV32IM -­ micro-­controller
Rocket
  RV64G - in-­order, single-­issue application core
BOOM
  RV64G -­ out-­of-­order, superscalar application core

## Slide 119
What is BOOM?
superscalar, out-of-order processor written in Berkeley’s Chisel RTL
It is synthesizable
It is parameterizable
We hope to use it as a plaOorm for architecture research
It is open-source!
  BOOM is a work-in-progress

## Slide 120
Chisel
Hardware Construction Language embedded in Scala
not a high-level synthesis language hardware module is a data structure in Scala
Full power of Scala for writing generators
  object-oriented programming
  factory objects, traits, overloading
  functional programming
  high-­order funs, anonymous funcs, currying
generated C++ simulator is 1:1 copy of Verilog designs
version 3.0 coming soon!
  uses an IR called FIRRTL

## Slide 121
BOOM Pipeline
in-­‐order
front-­‐half
out-­‐of-­‐order
back-­‐half
Fetch
Decode & Rename
Issue Window
Unified Physical Register File
Functional Unit

## Slide 122
BOOM Pipeline
PRF
  explicit renaming
  holds speculative and commi6ed data
  holds both x-­regs, f-­regs
split ROB/issue window design
Uniﬁed Issue Window
  holds all instructions
Fetch
Decode & Rename
Issue Window
Unified Physical Register File (PRF)
FPU
ALU
Rename Map Tables & Freelist
ROB
Commit

## Slide 123
Parameterized Superscalar
OR
= true
= true
= true
val exe_units = ArrayBuffer[ExecutionUnit]() exe_units += Module(new ALUExeUnit(is_branch_unit
, has_fpu
, has_mul
))
exe_units += Module(new ALUMemExeUnit(fp_mem_support = true
, has_div = true
))
Issue Select
Regfile
Writeback
dual-issue (5r,3w)
bypassing
ALU
div
Agen
LSU |  | D$
bypassing
ALU
FPU
bypass
network
Regfile
Read
imul
exe_units += Module(new ALUExeUnit(is_branch_unit = true))
exe_units += Module(new ALUExeUnit(has_fpu = true
, has_mul = true
))
exe_units += Module(new ALUExeUnit(has_div = true)) exe_units += Module(new MemExeUnit())
Issue Select
Regfile
Writeback
Quad-issue (9r,4w)
ALU
div
LSU
Agen
D$
ALU
imul
FPU
ALU
bypassing
network
Regfile bypass
Read

## Slide 124
Open-­‐source Berkeley RISC-V Processors
Abstract FunctionalUnit
  describes common IO
Pipelined/Unpipelined
  handles storing uop metadata, branch resolution, branch kills
Concrete Subclasses
  instantiates the actual expert-written FU
  no modiﬁcations required to get FU working with speculative OoO
  allows easy “stealing” of external code
Functional Unit
Pipelined
(req.ready ==true)
UnPipelined
ALU
(w/ optional Br Unit)
iMul/iDiv/ iRem
MemAddrCalc
FPU
iMul
fDiv/fSqrt
ALU
DFMA
SFMA
FPTo
Int
FPTo FP
IntTo FP

## Slide 125
Synthesizable
Targeting ASIC
Runs on FPGA
  Zynq zc706
Issue
Window
Physical Register File (5x3) (PRF)
ALU
Commit
wakeup
uop
tags
ROB
inst
Decode &
Rename
Fetch
2
2
2
2
2
FPU
ALU
LSU
Data cache
issue unit
fpu
dcache
uncore
icache
imul
rename
lsu
rob
regfile
regread
muldiv
alu
alu
rob
2-wide BOOM, 16kB L1 caches
1.2 mm2
TSMC 45nm floorplan
preliminary results

## Slide 126
Load/Store Unit
F st_mask forward_
std_idx
ROB
com_st_mask com_ld_mask
assoc search
fwd_std_idx
Age Logic
fwd_std_val
SDQ
val data
NACK
addrmatches
Address
Calculation
Adder
Store Address
Load Address
LOAD/STORE
UNIT
youngest store idx load depends on
Writeport
Register File
br kill
br kill
Data Array
Data
nack
kill request
TLB
vaddr
paddr
store address
woken-up load address
assoc search
woken-up load address
TLB load address
ECC/
Fmt
Mem Stage
Exe Stage
Data
cache
exceptions**
page fault
Addr
Data
Addr
ordering failures from store search
retry load address (needs translation)
retry store address (needs translation)
SAQ
A val addr V
LAQ
A val addr V E R
miss xcpt
TLB miss or !ready
kill*
Store unbusy†
ROB
br kill
nack
xcpt
st->ld addr match
TLB miss
WB Stage

## Slide 127
Question of the Day
How many in-order cores do you think take up the same area as an out-of-order core?

## Slide 128
How Many In-Order In The Same Area?

## Slide 129
Performance?

## Slide 130
Comparison against ARM
note: not to scale
Category | ARM Cortex-A9 | RISC-V BOOM-2w
ISA | 32-bit ARM v7 | 64-bit RISC-V v2 (RV64G)
Architecture | 2 wide, 3+1 issue Out-of- Order 8-stage | 2 wide, 3 issue Out-of-Order 6-stage
Performance | 3.59 CoreMarks/MHz | 3.91 CoreMarks/MHz
Process | TSMC 40GPLUS | TSMC 40GPLUS
Area with 32K caches | ~2.5 mm2 | ~1.00 mm2
Area efficiency | 1.4 CoreMarks/MHz/mm2 | 3.9 CoreMarks/MHz/mm2
Frequency | 1.4 GHz | 1.5 GHz
Power | 0.5-1.9 W (2 cores + L2) @ TSMC 40nm, 0.8-2.0 GHz | 0.25 W (1 core + L1) @ TSMC 45nm, 1 GHz
+9%!

## Slide 131
Repositories
BOOM
  https://github.com/ucb-bar/riscv-­boom
  just the BOOM core code
Rocket-­chip
  https://github.com/ucb-bar/rocket-chip
  the rest of the SoC
  chisel, rocket, uncore, junctions, riscv-­tools, fpga-zynq, etc.
  generates C++ emulator, verilog for FPGA
  http://riscv.org/tutorial-­hpca2015/riscv-­rocket-­chip-­tutorial-bootcamp-hpca2015.pdf (for more information)

## Slide 132
BOOM Quick-­start
"BOOM-­chip" is (currently) a branch of rocket-­chip
"make run" builds and runs riscv-tests suite
there are many diﬀerent CONFIGs available!
  rocket-­chip/src/main/scala/PrivateConﬁgs.scala
  rocket-­chip/boom/src/main/scala/conﬁgs.scala
  slightly diﬀerent conﬁgs for diﬀerent targets (CPP, FPGA, VLSI)
$ export ROCKETCHIP_ADDONS="boom"
$ git clone https://github.com/ucb-bar/rocket-chip.git
$ cd rocket-chip
$ git checkout boom
$ git submodule update --init
$ cd riscv-tools
$ git submodule update --init --recursive riscv-tests
$ cd ../emulator; make run CONFIG=BOOMCPPConfig

## Slide 133
How do you verify and debug BOOM?
parameterization makes this tough!
tested with:
  riscv-­tests
    (assembly functional tests + bare-­metal micro-benchmarks)
  CoreMark + riscv-­pk
  SPEC + Linux
  riscv-torture

## Slide 134
riscv-­torture
now open-­source!
  https://github.com/ucb-bar/riscv-torture
torture generates random tests to stress the core pipeline
runs test on Spike and your processor
  architectural register state dumped to memory on program termination
  diﬀ state
  if error found, ﬁnds smallest version of test that exhibits an error

## Slide 135
riscv-­torture quick-­start
$ git clone https://github.com/ucb-bar/rocket-chip.git
$ cd rocket-­‐chip
$ git submodule update --init
$ cd riscv-­‐tools
$ git submodule update --init --recursive riscv-tests
$ cd ../emulator; make run CONFIG=BOOMCPPConfig
Run Rocket-chip (BOOM-chip?)
$ cd rocket-chip
$ git clone https://github.com/ucb-bar/riscv-torture.git
$ cd riscv-torture
$ git submodule update --init
$ vim Makefile # change RTL_CONFIG=BOOMCPPConfig
$ make igentest # test that torture works, gen a single test
$ make cnight # run C++ emulator overnight
Run Torture

## Slide 136
Commit Logging
BOOM can generate commit logs
  (priv level, PC, inst, wb raddr, wb data)
Spike supports generating commit logs!
  conﬁgure Spike with "-­-enable-commitlog" ﬂag
  outputs to stderr
only semi-automated
  valid diﬀerences from Spike and hw
  e.g., spinning on LR+SC
# modify the build.sh in riscv-tools
build_project riscv-isa-sim --prefix=$RISCV --with-fesvr=$RISCV --enable-commitlog

## Slide 137
What documentation is available?
A design document is in progress
  https://github.com/ccelio/riscv-­boom-­doc
Wiki
  https://github.com/ucb-­bar/riscv-­boom/wiki

## Slide 138
Conclusion
BOOM is RV64G, runs SPEC on Linux on an FPGA
BOOM is ~10k loc and 4 person-­years of work
excellent platform for prototyping new ideas
now open-­source!
I$
Fetch Buffer
NPC
BHT
BP
Dc/Rn
BTB
IS/RF
EX
MUL/
DIV
D$
Fmt
WB
Out-of-order processing
WB
WB
branch redirects
Com
bypass
issue unit
fpu
dcache
uncore
icache
imul
rename
lsu
rob
regfile
regread
muldiv
alu
alu
rob