## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
考试范围
L2-binary
L3a-isa
L3b-machinecode
L4a-DSD
L4c-singlecycle
L5-pipeline
L6-7 Memory
L8-9 Parallelism
L10 Cache Coherence
L11-12 Complex Pipeline

## Slide 3
Summary of RISC-V Instruction Formats

## Slide 4
Maximum Clock Speed
Combinatorial
Logic
(CL)
Register
(flip-flops)
Optional Feedback
Output
Input
Clock
CL
tCL

## Slide 5
Maximum PC Clock Speed
Minimum cycle time:
Maximum clock rate:
Example: tsetup ≥ 15ps, tadd = 75ps, tclk-toQ ≥ 10ps
tmin ≥ 100ps
fclk-max ≤ 10GHz

## Slide 6
Timing Diagram for add
clock
1000
1004
PC
1004
1008
PC+4
add x1,x2,x3
add x6,x7,x9
inst[31:0]
Clock
time
Reg[2]
Reg[7]
Reg[rs1]
Reg[2]+Reg[3]
alu
Reg[7]+Reg[9]
Reg[3]
Reg[9]
Reg[rs2]
???
Reg[1]
Reg[2]+Reg[3]

## Slide 7
Single-Cycle RISC-V RV32I Datapath

## Slide 8
Control Logic Truth Table (incomplete)
Inst[31:0] | BrEq | BrLT | PCSel | ImmSel | BrUn | ASel | BSel | ALUSel | MemRW | RegWEn | WBSel
add | * | * | +4 | * | * | Reg | Reg | Add | Read | 1 | ALU
sub | * | * | +4 | * | * | Reg | Reg | Sub | Read | 1 | ALU
(R-R Op) | * | * | +4 | * | * | Reg | Reg | (Op) | Read | 1 | ALU
addi | * | * | +4 | I | * | Reg | Imm | Add | Read | 1 | ALU
lw | * | * | +4 | I | * | Reg | Imm | Add | Read | 1 | Mem
sw | * | * | +4 | S | * | Reg | Imm | Add | Write | 0 | *
beq | 0 | * | +4 | B | * | PC | Imm | Add | Read | 0 | *
beq | 1 | * | ALU | B | * | PC | Imm | Add | Read | 0 | *
bne | 0 | * | ALU | B | * | PC | Imm | Add | Read | 0 | *
bne | 1 | * | +4 | B | * | PC | Imm | Add | Read | 0 | *
blt | * | 1 | ALU | B | 0 | PC | Imm | Add | Read | 0 | *
bltu | * | 1 | ALU | B | 1 | PC | Imm | Add | Read | 0 | *
jalr | * | * | ALU | I | * | Reg | Imm | Add | Read | 1 | PC+4
jal | * | * | ALU | J | * | PC | Imm | Add | Read | 1 | PC+4
auipc | * | * | +4 | U | * | PC | Imm | Add | Read | 1 | ALU

## Slide 9
add Execution
1000
1004
PC
1004
1008
PC+4
add x1,x2,x3
add x6,x7,x9
inst[31:0]
Clock
Reg[2]
Reg[7]
Reg[rs1]
Reg[2]+Reg[3]
alu
Reg[7]+Reg[9]
Reg[3]
Reg[9]
Reg[rs2]
???
Reg[1]
Reg[2]+Reg[3]
+4
Add
addr
inst
IMEM
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Bsel
mem
alu
alu
=pc+4
=*
=1
=*
=0
=0
=add
=Read
=1
=*
=*
Reg[2]+Reg[3]
wb
Reg[7]+Reg[9]
add control
add control
Control logic

## Slide 10
Peer Instruction(s): Critical Path
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu
Critical path for a addi
R[rd] = R[rs1]+imm
tclk-q + tAdd + tIMEM + tReg + tBComp + tALU + tDMEM + tmux + tSetup
tclk-q + tIMEM + max{tReg, tImm} + tALU + 2tmux + tSetup
tclk-q + tIMEM + max{tReg, tImm} + tALU + 3tmux + tDMEM + tSetup
None of the above

## Slide 11
Pipelining with RISC-V
Phase | Pictogram | tstep Serial
Instruction Fetch |  | 200 ps
Reg Read |  | 100 ps
ALU |  | 200 ps
Memory |  | 200 ps
Register Write |  | 100 ps
tinstruction |  | 800 ps
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
tcycle Pipelined
200 ps
200 ps
200 ps
200 ps
200 ps
1000 ps

## Slide 12
Pipelining with RISC-V
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
 | Single Cycle | Pipelining
Timing | tstep = 100 … 200 ps | tcycle = 200 ps
 | Register access only 100 ps | All cycles same length
Instruction time, tinstruction | = tcycle = 800 ps | 1000 ps
Clock rate, fs | 1/800 ps = 1.25 GHz | 1/200 ps = 5 GHz
Relative speed | 1 x | 4 x

## Slide 13
Pipelined RISC-V RV32I Datapath
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
Must pipeline instruction along with data, so control operates correctly in each stage

## Slide 14
Each stage operates on different instruction
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 15
Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation
  Information is stored in pipeline registers for use by later stages

## Slide 16
Instructions interact with each other in pipeline
An instruction in the pipeline may need a resource being used by another instruction in the pipeline  structural hazard (结构冒险)
An instruction may depend on something produced by an earlier instruction
  Dependence may be for a data value  data hazard (数据冒险)
  Dependence may be for the next instruction’s address  control hazard (控制冒险) (branches, exceptions)
Handling hazards generally introduces bubbles into pipeline and reduces ideal CPI > 1

## Slide 17
Structural Hazard
Problem: Two or more instructions in the pipeline compete for access to a single physical resource
  Solution 1: Instructions take it in turns to use resource, some instructions have to stall
  Solution 2: Add more hardware to machine
    E.g., if two instructions both need a port to memory at same time, could avoid hazard by adding second port to memory
Can always solve a structural hazard by adding more hardware
Classic RISC 5-stage integer pipeline has no structural hazards by design
  Many RISC implementations have structural hazards on multi-cycle units such as multipliers, dividers, floating-point units, etc., and can have on register writeback ports

## Slide 18
Regfile Structural Hazards
Each instruction:
  can read up to two operands in decode stage
  can write one value in writeback stage
Avoid structural hazard by having separate “ports”
  two independent read ports and one independent write port
Three accesses per cycle can happen simultaneously

## Slide 19
Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Without separate memories, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
RISC ISAs (including RISC-V) designed to avoid structural hazards
  e.g. at most one memory access/instruction

## Slide 20
Data Hazard: Register Access
Separate ports, but what if write to same value as read?
Does sw in the example fetch the old or new value?
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)

## Slide 21
Register Access Policy
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Exploit high speed of register file (100 ps)
  WB updates value
  ID reads new value
Indicated in diagram by shading
Might not always be possible to write then read in same cycle, especially in high-frequency designs. Check assumptions in any question.

## Slide 22
Data Hazard: ALU Result
add s0, t1, t2
sub t2, s0, t5
or t6, s0, t3
instruction sequence
xor t5, t1, s0
sw s0, 8(t3)
5 |  |  |  |  |  |  |  | 
Value of s0
Without some fix, sub and or will calculate wrong result!
5
5
5
5/9
9

## Slide 23
Solution 1: Stalling暂停 (Interlock互锁)
Problem: Instruction depends on result from previous instruction
add s0, t0, t1 sub t2, s0, t3
Bubble:
  effectively NOP: affected pipeline stages do “nothing”

## Slide 24
Solution 2: Forwarding数据前递(Bypass旁路)
add t0, t1, t2
or t3, t0, t5
sub t6, t0, t3
instruction sequence
xor t5, t1, t0
sw t0, 8(t3)
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9
Value of t0
Forwarding: grab operand from pipeline stage,
rather than register file

## Slide 25
1) Detect Need for Forwarding (example)
add t0, t1, t2
or t3, t0, t5
sub t6, t0, t3
X
M
W
D
instX.rd
instD.rs1
Compare destination of older instructions in pipeline with sources of new instruction in decode stage.
Must ignore writes to x0!

## Slide 26
Forwarding Path

## Slide 27
Load Data Hazard
1 cycle stall unavoidable
forward
unaffected

## Slide 28
Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
RISC-V code for D=A+B; E=A+C;
Original Order:
lw t1, 0(t0)
lw t2, 4(t0)
add t3, t1, t2
sw t3, 12(t0)
lw t4, 8(t0)
add t5, t1, t4
sw t5, 16(t0)
Alternative:
lw t1, 0(t0)
lw t2, 4(t0)
lw t4, 8(t0)
add t3, t1, t2
sw t3, 12(t0)
add t5, t1, t4
sw t5, 16(t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 29
Control Hazards
What do we need to calculate next PC?
For Unconditional Jumps
  Opcode, PC, and offset
For Jump Register
  Opcode, Register value, and offset
For Conditional Branches
  Opcode, Register (for condition), PC and offset
For all other instructions
  Opcode and PC ( and have to know it’s not one of above )

## Slide 30
Branch Prediction
beq t0, t1, label
label: …..
…..
Taken branch
Guess next PC!
Check guess correct

## Slide 31
Solutions
Structural Hazards
  Solution 1: Instructions take it in turns to use resource
  Solution 2: Add more hardware to machine
    Regfile Structural Hazards: 2 read ports and 1 write port
    Memory Structural Hazards: dedicated caches
Data Hazards
  Register access: write-then-read
  ALU results: stalling (interlocking) and forwarding (bypassing)
  Load data harzards: stalling and rescheduling
Control Hazards
  Kill instructions
  Branch prediction

## Slide 32
Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM
latency: Register << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access (SRAM)
  if data Ï fast memory  high latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data

## Slide 33
Big Idea: Locality
Temporal Locality (locality in time)
  Go back to same book on desk multiple times
  If a memory location is referenced, then it will tend to be referenced again soon
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books on J.D. Salinger since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon

## Slide 34
Adding Cache to Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 35
Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Address
Tag
Data Block
Data
Byte
Data
Byte
Data
Byte
Line
100
304
6848
copy of main
memory
location 100
copy of main
memory
location 101
416

## Slide 36
Cache Terminology
hit: data appears in some block
  hit rate: the fraction of accesses found in the level
  hit time: time to access the level (consists of RAM access time + time to determine hit)
miss: data needs to be retrieved from a block in the lower level (e.g., block Y)
  miss rate = 1 - (hit rate)
  miss penalty: time to replace a block in the upper level + time to deliver the block to the processor
hit time << miss penalty
Abbreviation: “$” = cache (a Berkeley innovation!)

## Slide 37
Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
AMAT = Time for a hit + Miss rate × Miss penalty
miss penalty: time to fetch a block from lower memory level
  access time: function of latency
  transfer time: function of bandwidth b/w levels
    transfer one “cache line/block” at a time
    transfer at the size of the memory-bus width
Important Equation!

## Slide 38
Processor Address Fields Used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2(number of sets)
Size of Tag = Address size – Size of Index – log2(number of bytes/block)
Block offset
Set Index
Tag
Processor Address (32-bits total)

## Slide 39
Direct-Mapped Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 40
Cache Organization: Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low-order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the memory block in cache?
Compare the cache tag to the high-order 2 memory address bits to tell if the memory block is in the cache (provided valid bit is set)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits (xx) define the byte in the block (32b words)
Index

## Slide 41
Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 1K words
20
Tag
Index
8
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11. . . 4 . . . 0
Byte offset
20
Hit
What kind of locality are we taking advantage of?
2
Data
32
Word offset

## Slide 42
Ping Pong Cache Example: Direct-Mapped Cache w/4 Single-Word Blocks, Worst-Case Reference String
Consider the main memory address reference string of word numbers:
0 4 0 4 0 4 0 4
0
4
0
4
0
4
0
4
Start with an empty cache - all blocks initially marked as not valid

## Slide 43
Ping Pong Cache Example: Direct-Mapped Cache w/4 Single-Word Blocks, Worst-Case Reference String
Consider the main memory address reference string of word numbers:
0 4 0 4 0 4 0 4
0
4
0
4
0
4
0
4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping-pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses

## Slide 44
Example: 2-Way Set Associative $ (4 words = 2 sets x 2 ways per set)
0
Cache
Main Memory
Q: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)

## Slide 45
2-Way Set-Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t

## Slide 46
Ping Pong Cache Example: 4 Word 2-Way SA $, Same Reference String
Consider the main memory word reference string
0 4 0 4 0 4 0 4
0
4
0
4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping-pong effect in a direct-mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses

## Slide 47
Alternative Cache Organizations
“Fully Associative”: Block can go anywhere
  First design in lecture
  Note: No Index field, but one comparator/block
“Direct Mapped”: Block goes one place
  Note: Only 1 comparator
  Number of sets = number blocks
“N-way Set Associative”: N places for a block
  Number of sets = number of blocks / N
  N comparators
  Fully Associative: N = number of blocks
  Direct Mapped: N = 1

## Slide 48
Range of Set-Associative Caches
For a fixed-size cache and fixed block size, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number of ways) and halves the number of sets
  decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
Decreasing associativity, lower way, more sets
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity, higher way, less sets
Selects the set
Used for tag compare
Selects the word in the block
More Associativity (more ways)

## Slide 49
Total Cache Capacity =
Associativity * # of sets * block_size
Bytes = blocks/set * sets * Bytes/block
Byte Offset
Tag
Index
C = N * S * B
address_size = tag_size + index_size + offset_size
= tag_size + log2(S) + log2(B)
Double the Associativity: Number of sets?
tag_size? index_size? # comparators?
Double the Sets: Associativity?
tag_size? index_size? # comparators?

## Slide 50
Replacement Policy
In an associative cache, which block from a set should be evicted when the set becomes full?
Random
Least-Recently Used (LRU)
  LRU cache state must be updated on every access
  true implementation only feasible for small sets (2-way)
  pseudo-LRU binary tree often used for 4-8 way
First-In, First-Out (FIFO) a.k.a. Round-Robin
  used in highly associative caches
Not-Most-Recently Used (NMRU)
  FIFO with exception for most-recently used block or blocks
This is a second-order effect. Why?
Replacement only happens on misses

## Slide 51
Sources of Cache Misses (3 C’s)
Compulsory (cold start, first reference):
  1st access to a block, not a lot you can do about it
    If running billions of instructions, compulsory misses are insignificant
  misses that would occur even with infinite cache
Capacity:
  cache is too small to hold all data needed by the program
    Misses that would not occur with infinite cache
    misses that would occur even under perfect replacement policy
Conflict (collision):
  Misses that occur because of collisions due to line-placement strategy (multiple memory locations mapped to same cache set)
    Misses that would not occur with ideal fully associative cache

## Slide 52
Impact of Cache Performance and Complexity

## Slide 53
Local vs. Global Miss Rates
Local miss rate: fraction of references to a given level of a cache that miss
  Local Miss rate L2$ = L2$ Misses / L1$ Misses = L2$ Misses / total_L2_accesses
Global miss rate: the fraction of references that miss in all levels of a multilevel cache and go all the way to memory
  L2$ local miss rate >> than the global miss rate
Global Miss rate = L2$ Misses / Total Accesses
  = (L2$ Misses / L1$ Misses) × (L1$ Misses / Total Accesses)
  = Local Miss rate L2$ × Local Miss rate L1$
AMAT = Time for a hit + Miss rate × Miss penalty
AMAT = Time for a L1$ hit + (local) Miss rate L1$ × (Time for a L2$ hit + (local) Miss rate L2$ × L2$ Miss penalty)

## Slide 54
Handling Stores with Write-Through
Store instructions write to memory, changing values
Need to make sure cache and memory have same values on writes: two policies
1) Write-Through Policy: write cache and write through the cache to memory
  Every write eventually gets to memory
  Too slow, so include Write Buffer to allow processor to continue once data in Buffer
  Buffer updates memory in parallel to processor

## Slide 55
Handling Stores with Write-Back
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)

## Slide 56
Write-Through vs. Write-Back
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Easier to make reliable, since memory always has copy of data (big idea: Redundancy!)
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Usually reduces write traffic
  Harder to make reliable, sometimes cache has only copy of data

## Slide 57
Write Policy Choices
Cache Hit:
  Write through: writes both cache & memory on every access
    Generally higher memory traffic but simpler pipeline & cache design
  Write back: writes cache only, memory written only when dirty entry evicted
    A dirty bit per line reduces write-back traffic
    Must handle 0, 1, or 2 accesses to memory for each load/store
Cache Miss:
  No write allocate: only write to main memory
  Write allocate (aka fetch on write): fetch into cache
Common combinations:
  Write through and no write allocate
  Write back with write allocate

## Slide 58
Write Performance
Tag
Data
V
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
WE

## Slide 59
Reducing Write Hit Time
Problem: Writes take two cycles in memory stage, one cycle for tag check plus one cycle for data write if hit
Solutions:
Design data RAM that can perform read and write in one cycle, restore old value after tag miss
Fully-associative (CAM Tag) caches: Word line only enabled if hit
Pipelined writes: Hold write data for store in single buffer ahead of cache, write cache data during next store’s tag check

## Slide 60
Presence of L2 influences L1 design
Use smaller L1 if there is also L2
  Trade increased L1 miss rate for reduced L1 hit time
  Backup L2 reduces L1 miss penalty
  Reduces average access energy
Use simpler write-through L1 with on-chip L2
  Write-back L2 cache absorbs write traffic, doesn’t go off-chip
  At most one L1 miss request per L1 access (no dirty victim write back) simplifies pipeline control
  Simplifies coherence issues
  Simplifies error recovery in L1 (can use just parity bits in L1 and reload from L2 when parity error detected on L1 read)

## Slide 61
Cache Hits and Misses
1. 0x04 = 000 00 0100
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | *
1. Fully Associative Version:
Tag | LRU
00000 | * 01
Unique blocks accessed so far: 1
Compulsory Miss
Block size = 16 bytes

## Slide 62
Cache Hits and Misses
2. 0xD8 = 011 01 1000
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | 
011 | *
2. Fully Associative Version:
Tag | LRU
00000 | 00
01101 | * 01
Unique blocks accessed so far: 2
Compulsory Miss

## Slide 63
Cache Hits and Misses
3. 0x05 = 000 00 0101
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | *
011 | 
3. Fully Associative Version:
Tag | LRU
00000 | *01
01101 | 00
Unique blocks accessed so far: 1
Hit (the tag matches, the block is in the cache, we just want a different byte inside the block when compared to the first access)

## Slide 64
Cache Hits and Misses
4. 0x192 = 110 01 0010
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | 
110 | *
4. Fully Associative Version:
Tag | LRU
00000 | 00
01101 | 01
11001 | * 10
Unique blocks accessed so far: 3
Compulsory Miss: note that the block with tag 011 was evicted to make room for the new block with tag 110. This is the first time we are accessing this block from memory and it is therefore a compulsory miss (no way to avoid it)

## Slide 65
Cache Hits and Misses
5. 0xD4 = 011 01 0100
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | 
011 | *
5. Fully Associative Version:
Tag | LRU
00000 | 01
01101 | *10
11001 | 01
Unique blocks accessed so far: 3
Conflict Miss: tag 011 was evicted in the 4th step. Both blocks mapped to the same cache index (01) and there’s only space for 1 block in that index. Use a fully associative cache to avoid evicting the 011 block in step 4. Therefore, it’s a conflict miss.

## Slide 66
Cache Hits and Misses
6. 0x1BA = 110 11 1010
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | 
011 | 
110 | *
6. Fully Associative Version:
Tag | LRU
00000 | 01
01101 | 10
11001 | 01
11011 | * 11
Unique blocks accessed so far: 4
Compulsory Miss

## Slide 67
Cache Hits and Misses
7. 0x83 = 010 00 0011
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
010 | *
011 | 
110 | 
7. Fully Associative Version:
Tag | LRU
01000 | * 11
01101 | 01
11001 | 00
11011 | 10
Unique blocks accessed so far: 5
Compulsory Miss: this is the first time we are accessing this block from memory and it is therefore a compulsory miss (no way to avoid it). This could also count as a capacity miss because even if we made the cache fully associative, there was no way to avoid this miss.

## Slide 68
Cache Hits and Misses
8. 0x04 = 000 00 0100
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | *
011 | 
110 | 
8. Fully Associative Version:
Tag | LRU
01000 | 10
01101 | 00
00000 | * 11
11011 | 10
Unique blocks accessed so far: 5
Capacity Miss: this is not classified as a conflict miss because 5 unique blocks have been in/out of the cache so far. The only way to avoid this miss is to increase the cache size and it is therefore a capacity miss.

## Slide 69
Cache Hits and Misses
9. 0x191 = 110 01 0001
1. 0x00000004
2. 0x000000D8
3. 0x00000005
4. 0x00000192
5. 0x000000D4
6. 0x000001BA
7. 0x00000083
8. 0x00000004
9. 0x00000191
Tag | LRU
000 | 
110 | *
110 | 
9. Fully Associative Version:
Tag | LRU
01000 | 01
01101 | * 11
00000 | 10
11011 | 00
Unique blocks accessed so far: 5
Capacity Miss: this is not a conflict miss because 5 unique blocks have been in/out of the cache so far. Even if we used a fully associative cache that can store 4 blocks, we could not store all 5 blocks and would still miss this cache access. The only way to avoid this miss is to increase the cache size and it is therefore a capacity miss.

## Slide 70
Types of Parallelism in Applications
Instruction-level parallelism (ILP)
  Multiple instructions in execution at the same time, e.g., instruction pipelining
  Generated and managed by hardware (superscalar) or by compiler (VLIW)
  Limited in practice by data and control dependences, i.e., pipeline hazards
Thread-level or task-level parallelism (TLP)
  Multiple threads or instruction sequences from the same application can be executed concurrently
  Thread: sequence of instructions, with own program counter and processor state (e.g., register file)
  Multicore:
    Physical CPU: One thread (at a time) per CPU, in software OS switches threads typically in response to I/O events like disk read/write
    Logical CPU: Fine-grain thread switching, in hardware, when thread blocks due to cache miss/memory access
    Hyperthreading (aka Simultaneous Multithreading--SMT): Exploit superscalar architecture to launch instructions from different threads at the same time!
  Limited in practice by communication/synchronization overheads and by algorithm characteristics

## Slide 71
Types of Parallelism in Applications
Data-level parallelism (DLP)
  Instructions from a single stream operate concurrently on several data
  Limited by non-regular data manipulation patterns and by memory bandwidth
Transaction-level parallelism
  Multiple threads/processes from different transactions can be executed concurrently
  Limited by concurrency overheads

## Slide 72
Matrix Multiplication
C = A*B
Cij = Σk (Aik * Bkj)
A
B
C

## Slide 73
Flynn* Taxonomy, 1966
SIMD and MIMD are currently the most common parallelism in architectures – usually both in same system!
Most common parallel processing programming style: Single Program Multiple Data (“SPMD”)
  Single program that runs on all processors of a MIMD
  Cross-processor execution coordination using synchronization primitives

## Slide 74
Potential Parallel Performance (assuming software can use it)
Year | Cores | SIMD bits /Core | Core * SIMD bits | Total, e.g. FLOPs/Cycle
2003 | 2 | 128 | 256 | 4
2005 | 4 | 128 | 512 | 8
2007 | 6 | 128 | 768 | 12
2009 | 8 | 128 | 1024 | 16
2011 | 10 | 256 | 2560 | 40
2013 | 12 | 256 | 3072 | 48
2015 | 14 | 512 | 7168 | 112
2017 | 16 | 512 | 8192 | 128
2019 | 18 | 1024 | 18432 | 288
2021 | 20 | 1024 | 20480 | 320
2.5X
8X
20X
MIMD
SIMD
MIMD & SIMD
+2/
2yrs
2X/
4yrs
12
years
20 x in 12 years
201/12 = 1.28 x  28% per year or 2x every 3 years!
IF (!) we can use it

## Slide 75
Big Idea: Amdahl’s Law
Part not sped up
Part sped up
Example: The execution time of half of a program can be accelerated by a factor of 2. What is the program speed-up overall?
Speedup = TO / TE = 1 / ((1-F) + F/SE)
TO / TE = 1 / ((1-F) + F/SE) = 1/((1- 0.5)+0.5/2) = 1.33 << 2

## Slide 76
Maximum “Achievable” Speed-Up
Question: What is a reasonable # of parallel processors to speed up an algorithm with F = 95%? (i.e. 19/20th can be sped up)
a) Maximum speedup: Smax = 1/(1-0.95) = 20
but needs SE=∞!
Reasonable “engineering” compromise:
Equal time in sequential and parallel code: (1-F) = F/SE
SE = F/(1-F) = 0.95/0.05 = 20
S = 1/(0.05+0.05) = 10
Speedup = 1 / ((1-F) + F/SE)
(SE->∞) = 1/(1-F)

## Slide 77
SIMD Data Types
(Now also AVX-512 available)

## Slide 78
SIMD Vector Mode

## Slide 79
Vectorized Matrix Multiplication
Inner Loop:
for i …; i+=4
for j ...
i += 4

## Slide 80
Loop Unrolling
Compiler does the unrolling
How do you verify that the generated code is actually unrolled?
4 registers

## Slide 81
FPU versus Memory Access
How many floating-point operations does matrix multiply take?
  F = 2 x N3 (N3 multiplies, N3 adds)
How many memory load/stores?
  M = 3 x N2 (for A, B, C)
Many more floating-point operations than memory accesses
  q = F/M = 2/3 * N
  Good, since arithmetic is faster than memory access
  Let’s check the code …

## Slide 82
Memory Access Blocking

## Slide 83
Performance
N | Gflops |  |  | 
 | scalar | avx | unroll | blocking
32 | 1.30 | 4.56 | 12.95 | 13.80
160 | 1.30 | 5.47 | 19.70 | 21.79
480 | 1.32 | 5.27 | 14.50 | 20.17
960 | 0.91 | 3.64 | 6.91 | 15.82

## Slide 84
Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage
Appears to software (including OS) as multiple, albeit slower, CPUs
+1
2
Thread select
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR1
GPR1
GPR1
GPR1
X
Y
2
D$

## Slide 85
Multithreading Costs
Each thread requires its own user state
  PC
  GPRs
Also, needs its own system state
  Virtual-memory page-table-base register
  Exception-handling registers
Other overheads:
  Additional cache/TLB conflicts from competing threads
  (or add larger cache/TLB capacity)
  More OS overhead to schedule more threads (where do all these threads come from?)

## Slide 86
Hyperthreading
SMT (HT): Logical CPUs > Physical CPUs
  Run multiple threads at the same time per core
  Each thread has own architectural state (PC, Registers, etc.)
  Share resources (cache, instruction unit, execution units)
  Improves Core CPI (clock ticks per instruction)
  May degrade Thread CPI (Utilization/Bandwidth v. Latency)
  See http://dada.cs.washington.edu/smt/

## Slide 87
Multithreaded Categories

## Slide 88
Parallel Loops
Serial execution:
for (int i=0; i<100; i++) {
…
}
Parallel Execution:
for (int i=0; i<25; i++) { … } | for (int i=25; i<50; i++) { … } | for (int i=50; i<75; i++) { … } | for (int i=75; i<100; i++) { … }

## Slide 89
Parallel for in OpenMP
#include <omp.h>
#pragma omp parallel for
for (int i=0; i<100; i++) {
…
}

## Slide 90
OpenMP Example
$ gcc-5 -fopenmp for.c;./a.out
thread 0, i = 0
thread 1, i = 3
thread 2, i = 6
thread 3, i = 8
thread 0, i = 1
thread 1, i = 4
thread 2, i = 7
thread 3, i = 9
thread 0, i = 2
thread 1, i = 5
01 02 03 14 15 16 27 28 39 40

## Slide 91
OpenMP
C extension: no new language to learn
Multi-threaded, shared-memory parallelism
  Compiler Directives, #pragma
  Runtime Library Routines, #include <omp.h>
#pragma
  Ignored by compilers unaware of OpenMP
  Same source for multiple architectures
    E.g., same program for 1 & 16 cores
Only works with shared memory

## Slide 92
Example 2: Computing p
http://openmp.org/mp-documents/omp-hands-on-SC08.pdf

## Slide 93
Parallelize (2) …
Compute
  sum[0] and sum[1]
in parallel
Compute
  sum = sum[0] + sum[1]
sequentially
sum[0]
sum[1]

## Slide 94
Parallel p
Scale up: num_steps = 106
pi = 3.141592653590
You verify how many digits are correct …

## Slide 95
OpenMP Reduction
double avg, sum=0.0, A[MAX]; int i;
#pragma omp parallel for private ( sum )
for (i = 0; i <= MAX ; i++) sum += A[i];
avg = sum/MAX; // bug
Problem is that we really want sum over all threads!
Reduction: specifies that 1 or more variables that are private to each thread are subject of reduction operation at end of parallel region: reduction(operation:var) where
  Operation: operator to perform on the variables (var) at the end of the parallel region
  Var: One or more variables on which to perform scalar reduction.
double avg, sum=0.0, A[MAX]; int i;
#pragma omp for reduction(+ : sum)
for (i = 0; i <= MAX ; i++) sum += A[i];
avg = sum/MAX;

## Slide 96
Version 2: parallel for, reduction
#include <omp.h>
#include <stdio.h>
/static long num_steps = 100000;
double step;
void main ()
{ int i; double x, pi, sum = 0.0;
step = 1.0/(double) num_steps;
#pragma omp parallel for private(x) reduction(+:sum)
for (i=1; i<= num_steps; i++){
x = (i-0.5)*step;
sum = sum + 4.0/(1.0+x*x);
}
pi = sum;
printf ("pi = %6.8f\n", pi);
}
Notes: 我们在#pragma omp parallel for 后面加上了 reduction(+:sum)，它的意思是告诉编译器：下面的for循环你要分成多个线程跑，但每个线程都要保存变量sum的拷贝，循环结束后，所有线程把自己的sum累加起来作为最后的输出。

## Slide 97
Matrix Multiply in OpenMP
// C[M][N] = A[M][P] × B[P][N]
start_time = omp_get_wtime();
#pragma omp parallel for private(tmp, j, k)
for (i=0; i<M; i++){
for (j=0; j<N; j++){
tmp = 0.0;
for (k=0; k<P; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += A[i][k] * B[k][j];
}
C[i][j] = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Outer loop spread across N threads; inner loops inside a single thread

## Slide 98
Multiprocessor Caches
Memory is a performance bottleneck even with one processor
Use caches to reduce bandwidth demands on main memory
Each core has a local private cache holding data it has accessed recently
Only cache misses have to access the shared common memory
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O

## Slide 99
Shared Memory and Caches
What if?
  Processors 1 and 2 read Memory[1000] (value 20)
Processor 0
Processor 1
Processor 2
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000
20
1000
1000
1000
20

## Slide 100
Shared Memory and Caches
Now:
  Processor 0 writes Memory[1000] with 40
Processor 0
Processor 1
Processor 2
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000 20
1000 20
1000
1000 40
1000 40
Problem?

## Slide 101
Keeping Multiple Caches Coherent
Architect’s job: shared memory => keep cache values coherent
Idea: When any processor has cache miss or writes, notify other processors via interconnection network
  If only reading, many processors can have copies
  If a processor writes, invalidate any other copies
Write transactions from one processor, other caches “snoop” the common interconnect checking for tags they hold
  Invalidate any copies of same address modified in other cache

## Slide 102
Snoopy Cache, Goodman 1983
Idea: Have cache watch (or snoop upon) other memory transactions, and then “do the right thing”
Snoopy cache tags are dual-ported
Proc.
Cache
Snoopy read port
attached to Memory
Bus
Data
(lines)
Tags and
State
A
D
R/W
Used to drive Memory Bus
when Cache is Bus Master
A
R/W

## Slide 103
How Does HW Keep $ Coherent?
Each cache tracks state of each block in cache:
Shared: up-to-date data, other caches may have a copy
Modified: up-to-date data, changed (dirty), no other cache has a copy, OK to write, memory out-of-date
Exclusive: up-to-date data, no other cache has a copy, OK to write, memory up-to-date
  Avoids writing to memory if block replaced
  Supplies data on read instead of going to memory
Owner: up-to-date data, other caches may have a copy (they must be in Shared state)
  Only cache that supplies data on read instead of going to memory
Two Optional Performance Optimizations of Cache Coherency via New States

## Slide 104
Cache State-Transition Diagram The MSI protocol
M
S
I
M: Modified
S: Shared
I: Invalid
Each cache line has state bits
Address tag
state
bits
Write miss
(P1 gets line from memory)
Other processor
intent to write (P1 writes back)
Read miss
(P1 gets line from memory)
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Cache state in processor P1
Other processor reads
(P1 writes back)

## Slide 105
Two-Processor Example (Reading and writing the same cache line)
M
S
I
Write miss
Read
miss
P1 intent to write
P2 intent to write
P2 reads,
P1 writes back
P1 reads
or writes
P2 intent to write
P1
M
S
I
Write miss
Read
miss
P2 intent to write
P1 intent to write
P1 reads,
P2 writes back
P2 reads
or writes
P1 intent to write
P2
P1 reads
P1 writes
P2 reads
P2 writes
P1 writes
P2 writes
P1 reads
P1 writes

## Slide 106
MESI: An Enhanced MSI protocol increased performance for private data
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache line has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back

## Slide 107
Shared Memory and Caches
Example, now with cache coherence
  Processors 1 and 2 read Memory[1000]
  Processor 0 writes Memory[1000] with 40
Processor 0
Processor 1
Processor 2
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000 20
1000 20
Processor 0
Write
Invalidates
Other Copies
1000
1000 40
1000 40

## Slide 108
Read miss, to uncached or shared line
Directory Controller
DRAM Bank
CPU
Cache
1
Load request at head of CPU->Cache queue.
2
Load misses in cache.
3
Send ShReq message to directory.
4
Message received at directory controller.
5
Access state and directory for line. Line’s state is R, with zero or more sharers.
6
Update directory by setting bit for new processor sharer.
7
Send ShRep message with contents of cache line.
8
ShRep arrives at cache.
9
Update cache tag and data and return load data to CPU.
Interconnection Network
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 109
Write miss, to read shared line
Directory Controller
DRAM Bank
CPU
Cache
1
Store request at head of CPU->Cache queue.
2
Store misses in cache.
3
Send ExReq message to directory.
4
ExReq message received at directory controller.
5
Access state and directory for line. Line’s state is R, with some set of sharers.
6
Send one InvReq message to each sharer.
11
ExRep arrives at cache
12
Update cache tag and data, then store data from CPU
Interconnection Network
CPU
Cache
7
InvReq arrives at cache.
8
Invalidate cache line. Send InvRep to directory.
9
InvRep received. Clear down sharer bit.
10
When no more sharers, send ExRep to cache.
Multiple sharers
CPU
Cache
CPU
Cache
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 110
Directory Operation
Example: load with no sharers
Sharing vector
0
Line state
Memory
4
P0
L1
0
Line state
P1
L1
0
0
Line state
P2
L1
Line state
Load
Miss
10
0 | 0 | 10
4
Value
0
0
Cache states: 00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached 01 = shared
10 = modified
10

## Slide 111
Directory Operation
Example: load with sharers
Sharing vector
0
1
Line state
Memory
4
P0
L1
0
1
Line state
P1
L1
0
P2
L1
0
0
Line state
Cache states: 00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached 01 = shared
10 = modified
Load
Line state
Miss
0 | 10 | 1
4
4
Value
10

## Slide 112
Directory Operation
Example: store with sharers
Sharing vector
Memory
4
P0
L1
P1
L1
P2
L1
Line state 0 0
Cache states: 00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached 01 = shared
10 = modified
Miss
4
Line state 0 01
Acknowledge
64
Acknowledge
Line state
Store
Line state 10 01
Invalidate
10
01
0 | 1 | 01
Reply

## Slide 113
Directory Operation
Example: load with owner
Sharing vector
1
0
Line state
Memory
P0
L1
0
0
Line state
P1
L1
Line state
P2
L1
Cache states: 00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached 01 = shared
10 = modified
Load
Line state
4
6
Forward
Miss
01
10
6
Value
0
10
Acknowledge+Value
10
01
10
46

## Slide 114
Directory Coherence Protocol
Snooping coherence
  Global state of a memory line is the collection of its state in all caches, and there is no summary state anywhere
  All cache controllers monitor all other caches’ activities and maintain the state of their lines
  Requires a broadcast shared medium (e.g., bus or ring) that also maintains a total order of all transactions
  Bus acts as a serialization point to provide ordering
Directory coherence
  Global state of a memory line is the collection of its state in all caches, but there is a summary state at the directory
  Cache controllers do not observe all activity, but interact only with directory
  Can be implemented on scalable networks, where there is no total order and no simple broadcast, but only one-to-one communication
  Directory acts as a serialization point to provide ordering

## Slide 115
False Sharing
A cache line contains more than one word
Cache-coherence is done at the line-level and not word-level
Suppose M1 writes wordi and M2 writes wordk and i ≠ k but both words have the same line address.
What can happen?
state line addr data0 data1 ... dataN

## Slide 116
Example: True v. False Sharing v. Hit?
Assume X and Y in same cache line. P1 and P2 both read X and Y before.

## Slide 117
Issues in Complex Pipeline Control
Structural conflicts at the execution stage if some FPU or memory unit is not pipelined and takes more than one cycle
Structural conflicts at the write-back stage due to variable latencies of different functional units
Out-of-order write hazards due to variable latencies of different functional units
How to handle exceptions?
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPRs
FPRs

## Slide 118
Types of Data Hazards
Consider executing a sequence of
rk ← ri op rj
type of instructions
Data-dependence
      r3 ← r1 op r2 Read-after-Write
      r5 ← r3 op r4 (RAW) hazard
Anti-dependence
      r3 ← r1 op r2 Write-after-Read
      r1 ← r4 op r5 (WAR) hazard
Output-dependence
      r3 ← r1 op r2 Write-after-Write
      r3 ← r6 op r7 (WAW) hazard

## Slide 119
A Data Structure for Correct Issues Keeps track of the status of Functional Units
The instruction i at the Issue stage consults this table
  FU available? check the busy column
  RAW? search the dest column for i’s sources
  WAR? search the source columns for i’s destination
  WAW? search the dest column for i’s destination
An entry is added to the table if no hazard is detected;
An entry is removed from the table after Write-Back
Name Busy Op Dest Src1 Src2
  Int
  Mem
  Add1
  Add2
  Add3
  Mult1
  Mult2
  Div

## Slide 120
Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
  (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set by Issue stage and cleared by WB stage
Issue checks the instruction (opcode dest src1 src2)
  against the scoreboard (Busy & WP) to dispatch
  FU available?
  RAW?
  WAR?
  WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 121
Scoreboard Dynamics
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
  Functional Unit Status Registers Reserved
  Int(1) Add(1) Mult(3) Div(4) WB for Writes
t0 I1 f6 f6
t1 I2 f2 f6 f6, f2
t2 f6 f2 f6, f2 I2
t3 I3 f0 f6 f6, f0
t4 f0 f6 f6, f0 I1
t5 I4 f0 f8 f0, f8
t6 f8 f0 f0, f8 I3
t7 I5 f10 f8 f8, f10
t8 f8 f10 f8, f10 I5
t9 f8 f8 I4
t10 I6 f6 f6
t11 f6 f6 I6

## Slide 122
Out-of-order Completion In-order Issue
Latency
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMULT.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
in-order comp 1 2
out-of-order comp 1 2
1 2 3 4 3 5 4 6 5 6
2 3 1 4 3 5 5 4 6 6

## Slide 123
In-Order Issue Limitations: an example
latency
1 | LD | F2, | 34(R2) |  | 1
2 | LD | F4, | 45(R3) |  | long
3 | MULTD | F6, | F4, | F2 | 3
4 | SUBD | F8, | F2, | F2 | 1
5 | DIVD | F4, | F2, | F8 | 4
6 | ADDD | F10, | F6, | F4 | 1
1
2
3
4
5
6
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
Out-of-order: 1 (2,1) 4 4 . . . . 2 3 . . 3 5 . . . 5 6 6
Out-of-order execution did not allow any significant improvement!

## Slide 124
Issue Limitations: In-Order and Out-of-Order
latency
1
2
3
4
X
5
6
. . 5 6 6
1 | LD | F2, | 34(R2) |  |  | 1
2 | LD | F4, | 45(R3) |  |  | long
3 | MULTD | F6, | F4, |  | F2 | 3
4 | SUBD | F8, | F2, |  | F2 | 1
5 | DIVD | F4’, | F2, |  | F8 | 4
6 | ADDD | F10, | F6, |  | F4’ | 1
In-order: |  | 1 (2,1) . . . . . |  | . 2 3 4 4 3 5 . |  | 
Out-of-order: |  | 1 (2,1) 4 4 5 . . |  | . 2 (3,5) 3 6 6 |  | 
Any antidependence can be eliminated by renaming. (renaming  additional storage)
Can it be done in hardware?
yes!

## Slide 125
Register Renaming
Decode does register renaming and adds instructions to the issue stage reorder buffer (ROB)
  renaming makes WAR or WAW hazards impossible
Any instruction in ROB whose RAW hazards have been satisfied can be dispatched.
  Out-of-order or dataflow execution
IF
ID
WB
ALU
Fadd
Issue
Mem
Fmul

## Slide 126
Renaming & Out-of-order Issue An example
t1 t2
.
.
.
data / ti
Renaming table Reorder buffer
p data Ins# use exec op p1 src1 p2 src2
F1 F2 F3 F4 F5 F6 F7 F8
LD
F2,
LD F4,
MULTD F6, SUBD F8,
1
2
3
4
5
6
DIVD ADDD
34(R2)
45(R3) F4, F2
F2, F2
F4, F2, F8
F10, F6, F4
When are names in sources replaced by data?
Whenever an FU produces data
When can a name be reused?
Whenever an instruction completes

## Slide 127
Reorder Buffer Management
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 128
Renaming & Out-of-order Issue
An example
When are tags in sources
replaced by data?
When can a name be reused?
1 FLD f2, 34(x2)
2 FLD f4, 45(x3)
3 FMULT.D f6, f4, f2
4 FSUB.D f8, f2, f2
5 FDIV.D f4, f2, f8
6 FADD.D f10, f6, f4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
t3
t4
t5
.
.
data / ti
p data
f1
f2
f3
f4
f5
f6
f7
f8
Whenever an FU produces data
Whenever an instruction completes
t1
1 1 0 LD
t2
2 1 0 LD
5 1 0 DIV 1 v1 0 t4
4 1 0 SUB 1 v1 1 v1
t4
3 1 0 MUL 0 t2 1 v1
t3
t5
v1
1 1 1 LD
1 0
4 1 1 SUB 1 v1 1 v1
4 0
v4
5 1 0 DIV 1 v1 1 v4
2 1 1 LD
2 0
3 1 0 MUL 1 v2 1 v1

## Slide 129
In-Order Commit for Precise Exceptions
In-order Out-of-order
In-order
Fetch Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
Exception?
Inject handler PC
Instructions fetched and decoded into instruction reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile & memory, is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)

## Slide 130
Extensions for Precise Exceptions
Inst# use exec op p1 src1 p2 src2 pd dest data cause
ptr2 next to commit
ptr1 next available
Reorder buffer
add <pd, dest, data, cause> fields in the instruction template
commit instructions to reg file and memory in program order  buffers can be maintained circularly
on exception, clear reorder buffer by resetting ptr1=ptr2
(stores must wait for commit before updating memory)

## Slide 131
Control-Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
~ Loop length x pipeline width + buffers

## Slide 132
Reducing Control-Flow Penalty
Software solutions
  Eliminate branches - loop unrolling
    Increases the run length
  Reduce resolution time - instruction scheduling
    Compute the branch condition as early as possible (of limited value because branches often in critical path through code)
Hardware solutions
  Find something else to do (delay slots)
    Replaces pipeline bubbles with useful work (requires software cooperation) – quickly see diminishing returns
  Speculate, i.e., branch prediction
    Speculative execution of instructions beyond the branch
    Many advances in accuracy, widely used

## Slide 133
Branch Prediction
Motivation:
  Branch penalties limit performance of deeply pipelined processors
  Modern branch predictors have high accuracy
  (>95%) and can reduce branch penalties significantly
Required hardware support:
  Prediction structures:
    Branch history tables, branch target buffers, etc.
Mispredict recovery mechanisms:
  Keep result computation separate from commit
  Kill instructions following branch in pipeline
  Restore state to that following branch

## Slide 134
Static Branch Prediction
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64 typically reported as ~80% accurate
backward
90%
forward
50%

## Slide 135
Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 136
Branch Prediction Bits
Assume 2 BP bits per instruction
Change the prediction after two consecutive mistakes!
¬take
wrong
taken
¬ taken
taken
taken
taken
¬take
right
take
right
take
wrong
¬ taken
¬ taken
¬ taken
BP state:
(predict take/¬take) x (last prediction right/wrong)

## Slide 137
Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 138
Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 139
Limitations of BHTs
Only predicts branch direction. Therefore, cannot redirect fetch stream until after branch target is determined.
UltraSPARC-III fetch pipeline
Correctly predicted
taken branch penalty
Jump Register penalty
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
Remainder of execute pipeline
(+ another 6 stages)

## Slide 140
Branch Target Buffer (BTB)
Keep both the branch PC and target PC in the BTB
PC+4 is fetched if match fails
Only taken branches and jumps held in BTB
Next PC determined before branch fetched and decoded
2k-entry direct-mapped BTB
(can also be associative)
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 141
Combining BTB and BHT
BTB entries are considerably more expensive than BHT, but can redirect fetches at earlier stage in pipeline and can accelerate indirect branches (JR)
BHT can hold many more entries and is more accurate
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
BTB
BHT
BHT in later pipeline stage corrects when BTB misses a predicted taken branch
BTB/BHT only updated after branch resolves in E stage

## Slide 142
Mispredict Recovery
t
v
t
v
t
v
Register File
Reorder
Buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
r1
t
v
r2
Rename
Snapshots
Ptr2 next to commit
Ptr1 next available
rollback next available
Take snapshot of register rename table at each predicted branch, recover earlier snapshot if branch mispredicted

## Slide 143
Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy/Ivy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 144
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
ROB
Rename Table
Physical Regs
Free List
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<x1>
P8
p

## Slide 145
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8

## Slide 146
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1

## Slide 147
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3

## Slide 148
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2

## Slide 149
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4

## Slide 150
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 x1 P0
x addi P0 x3 P1
x sub p P6 p P5 x6 P3
x ld p P7 x1 P0
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x

## Slide 151
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 x6 P3
x addi P0 x3 P1
x addi P0 x3 P1
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x
p
p
<x3>
P7

## Slide 152
In-Order versus Out-of-Order Phases
Instruction fetch/decode/rename always in-order
  Need to parse ISA sequentially to get correct semantics
  Proposals for speculative OoO instruction fetch, e.g., Multiscalar. Predict control flow and data dependencies across sequential program segments fetched/decoded/executed in parallel, fixup if prediction wrong
Dispatch (place instruction into machine buffers to wait for issue) also always in-order
  Some use “Dispatch” to mean “Issue”, but not in these lectures

## Slide 153
In-Order Versus Out-of-Order Issue
In-order issue:
  Issue stalls on RAW dependencies or structural hazards, or possibly WAR/WAW hazards
  Instruction cannot issue to execution units unless all preceding instructions have issued to execution units
Out-of-order issue:
  Instructions dispatched in program order to reservation stations (or other forms of instruction buffer) to wait for operands to arrive, or other hazards to clear
  While earlier instructions wait in issue buffers, following instructions can be dispatched and issued out-of-order

## Slide 154
In-Order versus Out-of-Order Completion
All but the simplest machines have out-of-order completion, due to different latencies of functional units and desire to bypass values as soon as available
Classic RISC 5-stage integer pipeline just barely has in-order completion
  Load takes two cycles, but following one-cycle integer op completes at same time, not earlier
  Adding pipelined FPU immediately brings OoO completion

## Slide 155
In-Order versus Out-of-Order Commit
In-order commit supports precise traps, standard today
  Some proposals to reduce the cost of in-order commit by retiring some instructions early to compact reorder buffer, but this is just an optimized in-order commit
Out-of-order commit was effectively what early OoO machines implemented (imprecise traps) as completion irrevocably changed machine state
  i.e., complete == commit in these machines

## Slide 156
Bytes, Words, Blocks, Pages
E.g.: 16 KiB DRAM, 4 KiB Pages (for VM), 128 B blocks (for caches), 4 B words (for lw/sw)
Page 3
Page 2
Page 1
Page 0
16 KiB
Block 0
Block 31
Word 0
Word 31
1 of 1 Memory
1 of 4 Pages per Memory
1 of 32 Blocks per Page
Can think of memory as:
4 Pages, or
128 Blocks, or
4096 Words, or
16,384 Bytes
Can think of a page as:
32 Blocks, or
1024 Words