## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
New-School Machine Structures
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0

## Slide 3
Review: Single-Cycle RISC-V RV32I Datapath

## Slide 4
Review: Single Cycle Instruction Timing
IF | ID | EX | MEM | WB | Total
I-MEM | Reg Read | ALU | D-MEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps

## Slide 5
Review: Pipelining RISC-V RV32I Datapath
Instruction Fetch
(F)
Instruction Decode/Register Read
(D)
ALU Execute
(X)
Memory Access
(M)
Write
Back
(W)

## Slide 6
Components of a Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 7
Early Read-Only Memory Technologies
Punched cards, From early 1700s through Jaquard Loom, Babbage, and then IBM
Punched paper tape, instruction stream in Harvard Mk 1
IBM Card Capacitor ROS
IBM Balanced Capacitor ROS
Diode Matrix, EDSAC-2 µcode store

## Slide 8
Early Read/Write Main Memory Technologies
Williams Tube, Manchester Mark 1, 1947
Babbage, 1800s: Digits stored on mechanical wheels
Mercury Delay Line, Univac 1, 1951
Also, regenerative capacitor memory on Atanasoff-Berry computer, and rotating magnetic drum memory on IBM 650

## Slide 9
MIT Whirlwind Core Memory

## Slide 10
Core Memory
Core memory was first large scale reliable main memory
  invented by Forrester in late 40s/early 50s at MIT for Whirlwind project
Bits stored as magnetization polarity on small ferrite cores threaded onto two-dimensional grid of wires
Coincident current pulses on X and Y wires would write cell and also sense original state (destructive reads)
Robust, non-volatile storage
Used on space shuttle computers
Cores threaded onto wires by hand (25 billion a year at peak production)
Core access time ~ 1µs
DEC PDP-8/E Board,
4K words x 12 bits, (1968)

## Slide 11
Core Memory
Semiconductor memory began to be competitive in early 1970s
  Intel formed to exploit market for semiconductor memory
  Early semiconductor memory was Static RAM (SRAM). SRAM cell internals similar to a latch (cross-coupled inverters).
First commercial Dynamic RAM (DRAM) was Intel 1103
  1Kbit of storage on single chip
  charge on a capacitor used to hold value
Semiconductor memory quickly
replaced core in ‘70s

## Slide 12
One-Transistor Dynamic RAM [Dennard, IBM]
TiN top electrode (VREF)
Ta2O5 dielectric
W bottom
electrode
poly
word
line
access transistor
1-T DRAM Cell
word
bit
access transistor
Storage
capacitor (FET gate, trench, stack)
VREF

## Slide 13
Modern DRAM Structure
[Samsung, sub-70nm DRAM, 2004]

## Slide 14
DRAM Architecture
Bits stored in 2-dimensional arrays on chip
Modern chips have around 4-8 logical banks on each chip
  each logical bank physically implemented as many smaller arrays
Row Address Decoder
Col.
1
Col. 2M
Row 1
Row 2N
Column Decoder & Sense Amplifiers
M
N
N+M
bit lines
word lines
Memory cell (one bit)
D
Data

## Slide 15
DRAM Architecture
DIMM (Dual Inline Memory Module) contains multiple chips with clock/control/address signals connected in parallel (sometimes need buffers to drive signals to all chips)
Data pins work together to return wide word (e.g., 64-bit data bus using 16x4-bit parts)
Address lines multiplexed row/column address
Clock and control signals
Data bus
(4b,8b,16b,32b)
DRAM chip
~12
~7

## Slide 16
DRAM Packaging, Mobile Devices
[ Apple A4 package cross-section, iFixit 2010 ]
Two stacked DRAM die
Processor plus logic die
[ Apple A4 package on circuit board]

## Slide 17
DRAM Packaging Apple A10

## Slide 18
High-Bandwidth Memory in SX-Aurora
1.2TB/s HBM Bandwidth, 6 channels * 1024 bits/channel * 1.6 Gb/s/pin

## Slide 19
DRAM Operation
Three steps in read/write access to a given bank
Row access (RAS)
  decode row address, enable addressed row (often multiple Kb in row)
  bitlines share charge with storage cell
  small change in voltage detected by SAs which latch whole row of bits
  sense amplifiers drive bitlines full rail to recharge storage cells
Column access (CAS)
  decode column address to select small number of sense amplifier latches (4, 8, 16, or 32 bits depending on DRAM package)
  on read, send latched bits out to chip pins
  on write, change SA latches which then charge storage cells to required value
  can perform multiple column accesses on same row without another row access (burst mode)
Precharge
  charges bit lines to known value, required before next row access
Each step has a latency of around 15-20ns in modern DRAMs
Various DRAM standards (DDR, RDRAM) have different ways of encoding the signals for transmission to the DRAM, but all share same core architecture

## Slide 20
Double-Data Rate (DDR2) DRAM
Row
Column
Precharge
Row’
Data
200MHz Clock
400Mb/s Data Rate
[ Micron, 256Mb DDR2 SDRAM datasheet ]

## Slide 21
CPU-Memory Bottleneck
Performance of high-speed computers is usually limited by memory bandwidth & latency
Latency (time for a single access)
  Memory access time >> Processor cycle time
Bandwidth (number of accesses per unit time)
  if fraction m of instructions access memory
    1+m memory references / instruction
    CPI = 1 requires 1+m memory refs / cycle (assuming RISC-V ISA)
Memory
CPU

## Slide 22
Physical Size Affects Latency
Small Memory
CPU
Big Memory
CPU
Signals have further to travel
Fan out to more locations

## Slide 23
Why are Large Memories Slow? Library Analogy
Time to find a book in a large library
  Search a large card catalog – (mapping title/author to index number)
  Round-trip time to walk to the stacks and retrieve the desired book
Larger libraries worsen both delays
Electronic memories have same issue, plus the technologies used to store a bit slow down as density increases (e.g., SRAM vs. DRAM vs. Disk)
However what we want is a large yet fast memory!

## Slide 24
What To Do: Library Analogy
Write a report using library books
  E.g., works of J.D. Salinger
Go to library, look up relevant books, fetch from stacks, and place on desk in library
If need more, check them out and keep on desk
  But don’t return earlier books since might need them
You hope this collection of ~10 books on desk enough to write report, despite 10 being only 0.00001% of books in ZJU libraries

## Slide 25
Processor-DRAM Gap (Latency)
1980 microprocessor executes ~one instruction in same time as DRAM access
2017 microprocessor executes ~1000 instructions in same time as DRAM access
Slow DRAM access has disastrous impact on CPU performance!

## Slide 26
Relative Memory Cell Sizes
[ Foss, “Implementing Application-Specific Memory”, ISSCC 1996 ]
DRAM on memory chip
On-Chip SRAM in logic chip

## Slide 27
Big Idea: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down. Why?

## Slide 28
Typical Memory Hierarchy
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Second-Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s-1000 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)

## Slide 29
Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM
latency: Register << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access (SRAM)
  if data Ï fast memory  high latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data

## Slide 30
Management of Memory Hierarchy
Small/fast storage, e.g., registers
  Address usually specified in instruction
  Generally implemented directly as a register file
    but hardware might do things behind software’s back, e.g., stack management, register renaming
Larger/slower storage, e.g., main memory
  Address usually computed from values in register
  Generally implemented as a hardware-managed cache hierarchy (hardware decides what is kept in fast memory)
    but software may provide “hints”, e.g., don’t cache or prefetch

## Slide 31
Big Idea: Locality
Temporal Locality (locality in time)
  Go back to same book on desk multiple times
  If a memory location is referenced, then it will tend to be referenced again soon
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books on J.D. Salinger since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon

## Slide 32
Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality

## Slide 33
Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time (spatial locality) and repeatedly access that portion (temporal locality)
What program structures lead to temporal and spatial locality in instruction accesses?
In data accesses?
What structures defeat temporal and spatial locality in instruction and data accesses?

## Slide 34
Memory Reference Patterns
Address
Time
Instruction
fetches
Stack
accesses
Data
accesses
n loop iterations
subroutine call
subroutine return
argument access
vector access
scalar accesses

## Slide 35
Caches exploit both types of predictability:
Exploit temporal locality by remembering the contents of recently accessed locations.
  Keep recently referenced items at higher levels, future references satisfied quickly
Exploit spatial locality by fetching blocks of data around recently accessed locations.
  Bring neighbors of recently referenced to higher levels, future references satisfied quickly

## Slide 36
Cache

## Slide 37
Cache Philosophy
Programmer-invisible hardware mechanism gives illusion of speed of fastest memory with size of largest memory
  Works even if you have no idea what a cache is
  Performance-oriented programmers sometimes “reverse engineer” cache organization to design data structures and access patterns optimized for a specific cache design

## Slide 38
Memory Access without Cache
Load word instruction: lw t0,0(t1)
t1 contains 1022ten, Memory[1022] = 99
Processor issues address 1022ten to Memory
Memory reads word at address 1022ten (99)
Memory sends 99 to Processor
Processor loads 99 into register t0

## Slide 39
Adding Cache to Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 40
Memory Access with Cache
Load word instruction: lw t0,0(t1)
t1 contains 1022ten, Memory[1022] = 99
With cache: Processor issues address 1022ten to Cache
  Cache checks to see if has copy of data at address 1022ten
    If finds a match (Hit): cache reads 99, sends to processor
    No match (Miss): cache sends address 1022 to Memory
      Memory reads 99 at address 1022ten
      Memory sends 99 to Cache
      Cache replaces word with new 99
      Cache sends 99 to processor
  Processor loads 99 into register t0

## Slide 41
Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Address
Tag
Data Block
Data
Byte
Data
Byte
Data
Byte
Line
100
304
6848
copy of main
memory
location 100
copy of main
memory
location 101
416

## Slide 42
Cache Algorithm (Read)
Look at Processor Address, search cache tags to find match. Then either
Found in cache
a.k.a. HIT
Return copy
of data from
cache
Not in cache
a.k.a. MISS
Read block of data from
Main Memory
Wait …
Return data to processor
and update cache
Q: Which line do we replace?

## Slide 43
Cache “Tags”
Need way to tell if have copy of location in memory so that can decide on hit or miss
On cache miss, put memory address of block in “tag address” of cache block
  1022 placed in tag next to data from memory (99)
Tag | Data
252 | 12
1022 | 99
131 | 7
2041 | 20
From earlier
loads or stores

## Slide 44
Anatomy of a 16 Byte Cache, with 4 Byte Blocks
Operations:
  Cache Hit
  Cache Miss
  Refill cache from memory
Cache needs Address Tags to decide if Processor Address is a Cache Hit or Cache Miss
  Compares all four tags
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
44

## Slide 45
Cache Replacement
Suppose processor now requests location 511, which contains 11?
Doesn’t match any cache block, so must “evict” a resident block to make room
  Which block to evict?
Replace “victim” with new memory block at address 511
Tag | Data
252 | 12
1022 | 99
131 | 7
2041 | 20
least_recently used(LRU)

## Slide 46
Block Must be Aligned in Memory
Word blocks are aligned, so binary address of all words in cache always ends in 00two
How to take advantage of this to save hardware and energy?
Don’t need to compare last 2 bits of 32-bit byte address (comparator can be narrower)
  Don’t need to store last 2 bits of 32-bit byte address in Cache Tag (Tag can be narrower)

## Slide 47
Anatomy of a 32B Cache, 8B Blocks
Blocks must be aligned in pairs, otherwise could get same word twice in cache
  Tags only have even-numbered words
  Last 3 bits of address always 000two
  Tags, comparators can be narrower
Can get hit for either word in block
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
42
1947
12
130
2040
1000
7
20
-10

## Slide 48
Hardware Cost of Cache
Need to compare every tag to the Processor address
Comparators are expensive
Optimization: use two “sets” of data with a total of only 2 comparators
Use one Address bit to select which set
Compare only tags from selected set
Generalize to more sets
Processor
32-bit
Address
Tag
Data
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
Tag
Data
Set 0
Set 1
Tag
Data
Tag
Data

## Slide 49
Hardware Cost of Cache
Processor
32-bit
Address
32-bit
Data
32-bit
Address
32-bit
Data
Memory
1022
99
252
12
Set 0
Even
Word
Cache
7
20
131
2041
Set 1
Odd
Word
2 1 0
00
31 3
Byte in word (block)
Set Index
Tag
Compare