## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Sub-Matrix Multiplication or: Beating Amdahl’s Law
Blocking:
  Rearrange code to use values loaded in cache many times
  Only “few” accesses to slow main memory (DRAM) per floating point operation
  → throughput limited by FP hardware and cache, not slow DRAM
  P&H, RISC-V edition p. 465

## Slide 3
Memory Access Blocking

## Slide 4
Performance
N | Gflops |  |  | 
 | scalar | avx | unroll | blocking
32 | 1.30 | 4.56 | 12.95 | 13.80
160 | 1.30 | 5.47 | 19.70 | 21.79
480 | 1.32 | 5.27 | 14.50 | 20.17
960 | 0.91 | 3.64 | 6.91 | 15.82

## Slide 5
Improving Performance
Increase clock rate fs
  Reached practical maximum for today’s technology
  < 5GHz for general purpose computers
Lower CPI (cycles per instruction)
  SIMD, “instruction level parallelism”
Perform multiple tasks simultaneously
  Multiple CPUs, each executing different program
  Tasks may be related
    E.g. each CPU performs part of a big matrix multiplication
  or unrelated
    E.g. distribute different web http requests over different computers
    E.g. run pptx (view lecture slides) and browser (youtube) simultaneously
Do all of the above:
  High fs, SIMD, multiple parallel tasks
Today’s
lecture

## Slide 6
New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 7
Parallel Computer Architectures
Several separate computers,
some means for communication
(e.g., Ethernet)
Massive array of computers,
fast communication between processors
Multi-core CPU:
1 datapath in single chip
share L3 cache, memory, peripherals
Example: Hive machines
GPU “graphics processing unit”

## Slide 8
Example: CPU with Two Cores
Processor “Core” 1
Control
Datapath
PC
Registers
(ALU)
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor 0 Memory Accesses
Processor “Core” 2
Control
Datapath
PC
Registers
(ALU)
Processor 1 Memory Accesses

## Slide 9
Multiprocessor Execution Model
Each processor (core) executes its own instructions
Separate resources (not shared)
  Datapath (PC, registers, ALU)
  Highest level caches (e.g., 1st and 2nd)
Shared resources
  Memory (DRAM)
  Often 3rd level cache
    Often on same silicon chip
    But not a requirement
Nomenclature
  “Multiprocessor Microprocessor”
  Multicore processor
    E.g., four core CPU (central processing unit)
    Executes four different instruction streams simultaneously

## Slide 10
Transition to Multicore
Sequential App Performance
+50% per year, ~ 100x per decade

## Slide 11
Pixel 2 vs. iPhone 8

## Slide 12
Pixel 2 vs. iPhone 8
ALUs
nm
MHz
GFlops
2.35Ghz + 1.9Ghz, 64Bit Octa-Core

## Slide 13
Pixel 2 vs. iPhone 8

## Slide 14
Pixel 2 vs. iPhone 8

## Slide 15
Multiprocessor Execution Model
Shared memory
  Each “core” has access to the entire memory in the processor
  Special hardware keeps caches consistent
  Advantages:
    Simplifies communication in program via shared variables
  Drawbacks:
    Does not scale well:
      “Slow” memory shared by many “customers” (cores)
      May become bottleneck (Amdahl’s Law)
Two ways to use a multiprocessor:
  Job-level parallelism
    Processors work on unrelated problems
    No communication between programs
  Partition work of single task between several cores
    E.g., each performs part of large matrix multiplication

## Slide 16
Parallel Processing
It’s difficult!
It’s inevitable
  Only path to increase performance
  Only path to lower energy consumption (improve battery life)
In mobile systems (e.g., smart phones, tablets)
  Multiple cores
  Dedicated processors, e.g.,
    Motion processor, image processor, neural processor in iPhone 8 + X
    GPU (graphics processing unit)
Warehouse-scale computers
  Multiple “nodes”
    “Boxes” with several CPUs, disks per box
  MIMD (multi-core) and SIMD (e.g. AVX) in each node

## Slide 17
Potential Parallel Performance (assuming software can use it)
Year | Cores | SIMD bits /Core | Core * SIMD bits | Total, e.g. FLOPs/Cycle
2003 | 2 | 128 | 256 | 4
2005 | 4 | 128 | 512 | 8
2007 | 6 | 128 | 768 | 12
2009 | 8 | 128 | 1024 | 16
2011 | 10 | 256 | 2560 | 40
2013 | 12 | 256 | 3072 | 48
2015 | 14 | 512 | 7168 | 112
2017 | 16 | 512 | 8192 | 128
2019 | 18 | 1024 | 18432 | 288
2021 | 20 | 1024 | 20480 | 320
2.5X
8X
20X
MIMD
SIMD
MIMD & SIMD
+2/
2yrs
2X/
4yrs
12
years
20 x in 12 years
201/12 = 1.28 x  28% per year or 2x every 3 years!
IF (!) we can use it

## Slide 18
Programs Running on my Computer
PID TTY TIME CMD
220 ?? 0:04.34 /usr/libexec/UserEventAgent (Aqua)
222 ?? 0:10.60 /usr/sbin/distnoted agent
224 ?? 0:09.11 /usr/sbin/cfprefsd agent
229 ?? 0:04.71 /usr/sbin/usernoted
230 ?? 0:02.35 /usr/libexec/nsurlsessiond
232 ?? 0:28.68 /System/Library/PrivateFrameworks/CalendarAgent.framework/Executables/CalendarAgent
234 ?? 0:04.36 /System/Library/PrivateFrameworks/GameCenterFoundation.framework/Versions/A/gamed
235 ?? 0:01.90 /System/Library/CoreServices/cloudphotosd.app/Contents/MacOS/cloudphotosd
236 ?? 0:49.72 /usr/libexec/secinitd
239 ?? 0:01.66 /System/Library/PrivateFrameworks/TCC.framework/Resources/tccd
240 ?? 0:12.68 /System/Library/Frameworks/Accounts.framework/Versions/A/Support/accountsd
241 ?? 0:09.56 /usr/libexec/SafariCloudHistoryPushAgent
242 ?? 0:00.27 /System/Library/PrivateFrameworks/CallHistory.framework/Support/CallHistorySyncHelper
243 ?? 0:00.74 /System/Library/CoreServices/mapspushd
244 ?? 0:00.79 /usr/libexec/fmfd
246 ?? 0:00.09 /System/Library/PrivateFrameworks/AskPermission.framework/Versions/A/Resources/askpermissiond
248 ?? 0:01.03 /System/Library/PrivateFrameworks/CloudDocsDaemon.framework/Versions/A/Support/bird
249 ?? 0:02.50 /System/Library/PrivateFrameworks/IDS.framework/identityservicesd.app/Contents/MacOS/identityservicesd
250 ?? 0:04.81 /usr/libexec/secd
254 ?? 0:24.01 /System/Library/PrivateFrameworks/CloudKitDaemon.framework/Support/cloudd
258 ?? 0:04.73 /System/Library/PrivateFrameworks/TelephonyUtilities.framework/callservicesd
267 ?? 0:02.15 /System/Library/CoreServices/AirPlayUIAgent.app/Contents/MacOS/AirPlayUIAgent --launchd
271 ?? 0:03.91 /usr/libexec/nsurlstoraged
274 ?? 0:00.90 /System/Library/PrivateFrameworks/CommerceKit.framework/Versions/A/Resources/storeaccountd
282 ?? 0:00.09 /usr/sbin/pboard
283 ?? 0:00.90 /System/Library/PrivateFrameworks/InternetAccounts.framework/Versions/A/XPCServices/com.apple.internetaccounts.xpc/Contents/MacOS/com.apple.internetaccounts
285 ?? 0:04.72 /System/Library/Frameworks/ApplicationServices.framework/Frameworks/ATS.framework/Support/fontd
291 ?? 0:00.25 /System/Library/Frameworks/Security.framework/Versions/A/Resources/CloudKeychainProxy.bundle/Contents/MacOS/CloudKeychainProxy
292 ?? 0:09.54 /System/Library/CoreServices/CoreServicesUIAgent.app/Contents/MacOS/CoreServicesUIAgent
293 ?? 0:00.29 /System/Library/PrivateFrameworks/CloudPhotoServices.framework/Versions/A/Frameworks/CloudPhotoServicesConfiguration.framework/Versions/A/XPCServices/com.apple.CloudPhotosConfiguration.xpc/Contents/MacOS/com.apple.CloudPhotosConfiguration
297 ?? 0:00.84 /System/Library/PrivateFrameworks/CloudServices.framework/Resources/com.apple.sbd
302 ?? 0:26.11 /System/Library/CoreServices/Dock.app/Contents/MacOS/Dock
303 ?? 0:09.55 /System/Library/CoreServices/SystemUIServer.app/Contents/MacOS/SystemUIServer
… 156 total at this moment
How does my laptop do this?
Imagine doing 156 assignments all at the same time!

## Slide 19
Threads
Sequential flow of instructions that performs some task
  Up to now we just called this a “program”
Each thread has:
  Dedicated PC (program counter)
  Separate registers
  Accesses the shared memory
Each physical core provides one (or more)
  Hardware threads that actively execute instructions
  Each executes one “hardware thread”
Operating system multiplexes multiple
  Software threads onto the available hardware threads
  All threads except those mapped to hardware threads are waiting

## Slide 20
Operating System Threads
Give illusion of many “simultaneously” active threads
Multiplex software threads onto hardware threads:
  Switch out blocked threads (e.g., cache miss, user input, network access)
  Timer (e.g., switch active thread every 1 ms)
Remove a software thread from a hardware thread by
  Interrupting its execution
  Saving its registers and PC to memory
Start executing a different software thread by
  Loading its previously saved registers into a hardware thread’s registers
  Jumping to its saved PC

## Slide 21
Example: Four Cores
Thread pool:
List of threads competing for processor
OS maps threads to cores and schedules
logical (software) threads
Core 2
Each “Core” actively runs one instruction stream at a time
Core 1
Core 3
Core 4

## Slide 22
Multithreading
Typical scenario:
  Active thread encounters cache miss
  Active thread waits ～ 1000 cycles for data from DRAM
  → switch out and run different thread until data available
Problem
  Must save current thread state and load new thread state
  PC, all registers (could be many, e.g. AVX)
  → must perform switch in ≪1000 cycles
Can hardware help?
  Moore’s Law: transistors are plenty

## Slide 23
Types of Parallelism in Applications
Instruction-level parallelism (ILP)
  Multiple instructions in execution at the same time, e.g., instruction pipelining
  Generated and managed by hardware (superscalar) or by compiler (VLIW)
  Limited in practice by data and control dependences, i.e., pipeline hazards
Thread-level or task-level parallelism (TLP)
  Multiple threads or instruction sequences from the same application can be executed concurrently
  Thread: sequence of instructions, with own program counter and processor state (e.g., register file)
  Multicore:
    Physical CPU: One thread (at a time) per CPU, in software OS switches threads typically in response to I/O events like disk read/write
    Logical CPU: Fine-grain thread switching, in hardware, when thread blocks due to cache miss/memory access
    Hyperthreading (aka Simultaneous Multithreading--SMT): Exploit superscalar architecture to launch instructions from different threads at the same time!
  Limited in practice by communication/synchronization overheads and by algorithm characteristics

## Slide 24
Types of Parallelism in Applications
Data-level parallelism (DLP)
  Instructions from a single stream operate concurrently on several data
  Limited by non-regular data manipulation patterns and by memory bandwidth
Transaction-level parallelism
  Multiple threads/processes from different transactions can be executed concurrently
  Limited by concurrency overheads

## Slide 25
CDC 6600 Peripheral Processors (Cray, 1964)
First multithreaded hardware
10 “virtual” I/O processors
Fixed interleave on simple pipeline
Pipeline has 100ns cycle time
Each virtual processor executes one instruction every 1000ns
Accumulator-based instruction set to reduce processor state

## Slide 26
Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage
Appears to software (including OS) as multiple, albeit slower, CPUs
+1
2
Thread select
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR1
GPR1
GPR1
GPR1
X
Y
2
D$

## Slide 27
Multithreading Costs
Each thread requires its own user state
  PC
  GPRs
Also, needs its own system state
  Virtual-memory page-table-base register
  Exception-handling registers
Other overheads:
  Additional cache/TLB conflicts from competing threads
  (or add larger cache/TLB capacity)
  More OS overhead to schedule more threads (where do all these threads come from?)

## Slide 28
Thread Scheduling Policies
Fixed interleave (CDC 6600 PPUs, 1964)
  Each of N threads executes one instruction every N cycles
  If thread not ready to go in its slot, insert pipeline bubble
Software-controlled interleave (TI ASC PPUs, 1971)
  OS allocates S pipeline slots amongst N threads
  Hardware performs fixed interleave over S slots, executing whichever thread is in that slot
Hardware-controlled thread scheduling (HEP, 1982)
  Hardware keeps track of which threads are ready to go
  Picks next thread to execute based on hardware priority scheme

## Slide 29
Denelcor HEP (Burton Smith, 1982)
First commercial machine to use hardware threading in main CPU
  120 threads per processor
  10 MHz clock rate
  Up to 8 processors
  precursor to Tera MTA (Multithreaded Architecture)

## Slide 30
Simultaneous Multithreading (SMT) for OoO Superscalars
Techniques presented so far have all been “vertical” multithreading where each pipeline stage works on one thread at a time
SMT uses fine-grain control already present inside an OoO superscalar to allow instructions from multiple threads to enter execution on same clock cycle. Gives better utilization of machine resources.

## Slide 31
Superscalar Machine Efficiency
Issue width
Time
Completely idle cycle (vertical waste)
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)

## Slide 32
Vertical Multithreading
Cycle-by-cycle interleaving removes vertical waste, but leaves some horizontal waste
Issue width
Time
Second thread interleaved cycle-by-cycle
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)

## Slide 33
Chip Multiprocessing (CMP)
What is the effect of splitting into multiple processors?
  reduces horizontal waste,
  leaves some vertical waste, and
  puts upper limit on peak throughput of each thread.
Issue width
Time

## Slide 34
Ideal Superscalar Multithreading [Tullsen, Eggers, Levy, UW, 1995]
Interleave multiple threads to multiple issue slots with no restrictions
Issue width
Time

## Slide 35
Hyperthreading
SMT (HT): Logical CPUs > Physical CPUs
  Run multiple threads at the same time per core
  Each thread has own architectural state (PC, Registers, etc.)
  Share resources (cache, instruction unit, execution units)
  Improves Core CPI (clock ticks per instruction)
  May degrade Thread CPI (Utilization/Bandwidth v. Latency)
  See http://dada.cs.washington.edu/smt/

## Slide 36
Multithreaded Categories

## Slide 37
Initial Performance of SMT
Pentium-4 Extreme SMT yields 1.01 speedup for SPECint_rate benchmark and 1.07 for SPECfp_rate
  Pentium-4 is dual-threaded SMT
  SPECRate requires that each SPEC benchmark be run against a vendor-selected number of copies of the same benchmark
Running on Pentium-4 each of 26 SPEC benchmarks paired with every other (262 runs) speed-ups from 0.90 to 1.58; average was 1.20
Power 5, 8-processor server 1.23 faster for SPECint_rate with SMT, 1.16 faster for SPECfp_rate
Power 5 running 2 copies of each app speedup between 0.89 and 1.41
  Most gained some
  Fl.Pt. apps had most cache conflicts and least gains

## Slide 38
Bulpin et al, “Multiprogramming Performance of Pentium 4 with Hyper-Threading”
SMT Performance: Application Interaction
Not affected by other programs

## Slide 39
SMT Performance: Application Interaction
Bulpin et al, “Multiprogramming Performance of Pentium 4 with Hyper-Threading”
Doesn’t play nice

## Slide 40
SMT Performance: Application Interaction
Bulpin et al, “Multiprogramming Performance of Pentium 4 with Hyper-Threading”
Very sensitive to second program

## Slide 41
Hardware Assisted Software Multithreading
Two copies of PC and Registers inside processor hardware
Looks identical to two processors to software (hardware thread 0, hardware thread 1)
Hyperthreading:
  Both threads can be active simultaneously
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor (1 Core, 2 Threads)
Control
Datapath
PC 0
Registers 0
(ALU)
PC 1
Registers 1

## Slide 42
Multithreading
Logical threads
  ≈ 1% more hardware, ≈ 10% (?) better performance
    Separate registers
    Share datapath, ALU(s), caches
Multicore
  => Duplicate Processors
  ≈50% more hardware, ≈2X better performance?
Modern machines do both
  Multiple cores with multiple threads per core

## Slide 43
Randy’s (Rather Old) Mac Air
$ sysctl -a | grep hw
hw.model = Core i7, 4650U
…
hw.physicalcpu: 2
hw.logicalcpu: 4
…
hw.cpufrequency = 1,700,000,000
hw.physmem = 8,589,934,592 (8 Gbytes) ...
hw.cachelinesize = 64
hw.l1icachesize: 32,768
hw.l1dcachesize: 32,768
hw.l2cachesize: 262,144
hw.l3cachesize: 4,194,304
Every machine is multicore,
Even your phone!

## Slide 44
Hive Machines
hw.model = Core i7 4770K
hw.physicalcpu: 4
hw.logicalcpu: 8
…
hw.cpufrequency = 3,900,000,000
hw.physmem = 34,359,738,368
hw.cachelinesize = 64
hw.l1icachesize: 32,768
hw.l1dcachesize: 32,768
hw.l2cachesize: 262,144
hw.l3cachesize: 8,388,608
Therefore, should try up to 8 threads to see if performance gain even though only 4 cores

## Slide 45
Example: 6 Cores, 24 Logical Threads
Thread pool:
List of threads competing for processor
OS maps threads to cores and schedules
logical (software) threads
Thread 1
Core 2
Thread 2
Thread 3
Thread 4
Thread 1
Core 6
Thread 2
Thread 3
Thread 4
Thread 1
Core 4
Thread 2
Thread 3
Thread 4
Thread 1
Core 5
Thread 2
Thread 3
Thread 4
Thread 1
Core 3
Thread 2
Thread 3
Thread 4
Thread 1
Core 1
Thread 2
Thread 3
Thread 4
4 Logical threads per core (hardware) thread

## Slide 46
Languages Supporting Parallel Programming
ActorScript | Concurrent Pascal | JoCaml | Orc
Ada | Concurrent ML | Join | Oz
Afnix | Concurrent Haskell | Java | Pict
Alef | Curry | Joule | Reia
Alice | CUDA | Joyce | SALSA
APL | E | LabVIEW | Scala
Axum | Eiffel | Limbo | SISAL
Chapel | Erlang | Linda | SR
Cilk | Fortan 90 | MultiLisp | Stackless Python
Clean | Go | Modula-3 | SuperPascal
Clojure | Io | Occam | VHDL
Concurrent C | Janus | occam-π | XC
Which one to pick?

## Slide 47
Why So Many Parallel Programming Languages?
Why “intrinsics”?
  TO Intel: fix your #()&$! Compiler!
It’s happening ... but
  SIMD features are continually added to compilers (Intel, gcc)
  Intense area of research
  Research progress:
    20+ years to translate C into good (fast!) assembly
    How long to translate C into good (fast!) parallel code?
      General problem is very hard to solve
      Present state: specialized solutions for specific cases
      Your opportunity to become famous!

## Slide 48
Review: Why Parallelism?
Only path to performance is parallelism
  Clock rates flat or declining
  SIMD: 2X width every 3-4 years
    AVX-512 2015, 1024b in 2018? 2019?
  MIMD: Add 2 cores every 2 years (2, 4, 6, 8, 10, …) Intel Broadwell-Extreme (2Q16): 10 Physical CPUs, 20 Logical CPUs
Key challenge: craft parallel programs with high performance on multiprocessors as # of processors increase – i.e., that scale
  Scheduling, load balancing, time for synchronization, overhead for communication

## Slide 49
Parallel Programming Languages
Number of choices is indication of
  No universal solution
    Needs are very problem specific
  E.g.,
    Scientific computing/machine learning (matrix multiply)
    Webserver: handle many unrelated requests simultaneously
    Input / output: it’s all happening simultaneously!
Specialized languages for different tasks
  Some are easier to use (for some problems)
  None is particularly ”easy” to use

## Slide 50
Parallel Loops
Serial execution:
for (int i=0; i<100; i++) {
…
}
Parallel Execution:
for (int i=0; i<25; i++) { … } | for (int i=25; i<50; i++) { … } | for (int i=50; i<75; i++) { … } | for (int i=75; i<100; i++) { … }

## Slide 51
OpenMP Building Block: for loop
for (i=0; i<max; i++) zero[i] = 0;
Breaks for loop into chunks, and allocate each to a separate thread
  e.g. if max = 100 with 2 threads: assign 0-49 to thread 0, and 50-99 to thread 1
Must have relatively simple “shape” for an OpenMP-aware compiler to be able to parallelize it
  Necessary for the run-time system to be able to determine how many of the loop iterations to assign to each thread
No premature exits from the loop allowed
  i.e. No break, return, exit, goto statements
In general, don’t jump outside of any pragma block

## Slide 52
Parallel for in OpenMP
#include <omp.h>
#pragma omp parallel for
for (int i=0; i<100; i++) {
…
}

## Slide 53
OpenMP Example
$ gcc-5 -fopenmp for.c;./a.out
thread 0, i = 0
thread 1, i = 3
thread 2, i = 6
thread 3, i = 8
thread 0, i = 1
thread 1, i = 4
thread 2, i = 7
thread 3, i = 9
thread 0, i = 2
thread 1, i = 5
01 02 03 14 15 16 27 28 39 40

## Slide 54
OpenMP
C extension: no new language to learn
Multi-threaded, shared-memory parallelism
  Compiler Directives, #pragma
  Runtime Library Routines, #include <omp.h>
#pragma
  Ignored by compilers unaware of OpenMP
  Same source for multiple architectures
    E.g., same program for 1 & 16 cores
Only works with shared memory

## Slide 55
OpenMP Parallel for pragma
#pragma omp parallel for
for (i=0; i<max; i++) zero[i] = 0;
Master thread creates additional threads, each with a separate execution context
All variables declared outside for loop are shared by default, except for loop index which is implicitly private per thread
Implicit “barrier” synchronization at end of for loop
Divide index regions sequentially per thread
  Thread 0 gets 0, 1, …, (max/n)-1;
  Thread 1 gets max/n, max/n+1, …, 2*(max/n)-1
  Why?

## Slide 56
OpenMP Programming Model
Fork - Join Model:
OpenMP programs begin as single process (master thread)
  Sequential execution
When parallel region is encountered
  Master thread “forks” into team of parallel threads
  Executed simultaneously
  At end of parallel region, parallel threads ”join”, leaving only master thread
Process repeats for each parallel region
  Amdahl’s Law?

## Slide 57
What Kind of Threads?
OpenMP threads are operating system (software) threads
OS will multiplex requested OpenMP threads onto available hardware threads
Hopefully each gets a real hardware thread to run on, so no OS-level time-multiplexing
But other tasks on machine compete for hardware threads!